## Slide 1: Identification of a servo-motor model from experimental data
Yue DANG
Guide by Prof. Carlo Novara

## Slide 2: List of Content
Introduction
  Introduction of the servo-motor system
  Introduction of the Hammerstein Wiener model
System identification applied to simulated servo-motor system
  Simulated servo-motor system
  Identification with the Hammerstein Wiener model
  Simulated result
System identification applied to real measurement
  System identification with single measurement
  System identification with group measurements
  Coverage Issue Discussion
Conclusion

## Slide 3: Introduction of the servo-motor system
Servo-motor system in arc-welding robot
The welding robot is controlling the current input of the servo-motor system to drive the welding head movement.
The current input to the displacement of the head is non-linear
The number of measurements of the current-to-displacement is limited

## Slide 4: Introduction of the Hammerstein Wiener model
Hammerstein Wiener Model
To identify a model with input and output, the system identification method is needed.
The Hammerstein Wiener model is designed for the non-linear electronic system.
The H-W model is consisting of three sub-blocks: nonlinear, linear and nonlinear.
B(nb)/F(nk)

## Slide 5: Simulated servo-motor system
Simulated servo-motor system
Target:
  Generate a nonlinear system with:
    Input: Current [A]
    Output: Displacement [mm]
  Identify a model with H-W method
  Verify the identified model result

## Slide 6: Identification with the Hammerstein Wiener model
Identification Steps:
  Generate displacement with input current
  Identify the HW system with input and output (current and displacement), considering the parameter combinations.
  Generate displacement based on the same current input and the identified system.
  Compare the result of the original displacement measurement and the identified measurement.
Identification and verification

## Slide 7: Simulated result

## Slide 8: System identification with single measurement
Single Measurement steps
Identification of the model:
  Using single data set to identify models based on the combination of parameter nb and nk.
  Self-cross check of the identified model with the same measurement data set (n), and choose the best one or several identified models.
Verification of the model:
  Applying the input current of each step datasets (m), and obtain the identified model displacement output
  Verification of the result with RMSD method based on measured displacement and the identified model displacement.

## Slide 9: System identification with single measurement
NLHW

## Slide 10: System identification with single measurement
Single Measurement steps
The result of single identified model cross check with itself shows a perfect result.
The best self-fitted model may lead to an overfitting, which shows poor performance to the other data set.

## Slide 11: Measurement data set choosing
Measurement data sets
Limited on measurements
  23 sinusoidal data sets
  15 step data sets
Data sets segmentation for identification, validation and test
  12 data sets used for identification and cross-validation
  3 data sets used for testing
Delay\Ampl. | 2 | 4 | 6 | 8 | 10
0 | #1 | #2 | #3 | #4 | #5
100 | #6 | #7 | #8 | #9 | #10
300 | #11 | #12 | #13 | #14 | #15

## Slide 12: System identification with Group measurement
Group Measurement steps
Group of data sets
Identification of the model:
  Same as the single measurement
Verification of the model:
  Additionally counting the total number of data sets below the RMSD threshold
RMSD=0.004
RMSD=0.01
RMSD=0.04

## Slide 13: System identification with Group measurement
Chart: RMSD Value for Test Data Set
Test5 | 0.16769 | 0.093722 | 0.11384 | 0.067228
Test10 | 0.090449 | 0.038308 | 0.043066 | 0.027559
Test11 | 0.0053714 | 0.025346 | 0.0076735 | 0.0067525
Identification Model\Test Data Set | nb | nk | Step Data Coverage | Test 5 | Test 10 | Test 11
6 | 3 | 7 | 6 | 0.168 | 0.0904 | 0.0054
6-8 | 4 | 3 | 7 | 0.094 | 0.0383 | 0.0253
6-8-1 | 1 | 6 | 8 | 0.114 | 0.0431 | 0.0077
6-8-1-12 | 1 | 5 | 8 | 0.067 | 0.0276 | 0.0068
With the increasing of grouping data sets, the model accuracy is increasing.
The grouping method is applicable to identify a model to cover more data sets.

## Slide 14: System identification with Group measurement Combination Model 1
As proved in the previous chapter, the same method is applied to identify a step data sets based model: combination model 1 (6-9-1-8)
 | Step Data Coverage
6 | 7
6-9 | 8
6-9-1 | 8
6-9-1-8 | 8
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
6 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0
6-9 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
6-9-1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0
6-9-1-8 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 0
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38
6 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
6-9 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
6-9-1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
6-9-1-8 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
The same method is applied to identify a step and sin data sets based model: combination model 2 (20-16-9-5-35-7)
 | Step & Sin Data Coverage
20 | 14
20-16 | 18
20-16-9 | 19
20-16-9-5 | 20
20-16-9-5-35 | 23
20-16-9-5-35-7 | 23
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38
20 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
20-16 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0
20-16-9 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0
20-16-9-5 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0
20-16-9-5-35 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
20-16-9-5-35-7 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0

## Slide 15: System identification with Group measurement Combination Model 1&2
 | Step Data Coverage
6 | 6
6-9 | 8
6-9-1 | 8
6-9-1-8 | 8

## Slide 16: System identification with Group measurement Combination Model 1&2
 | Step & Sin Data Coverage
20 | 14
20-16 | 18
20-16-9 | 19
20-16-9-5 | 20
20-16-9-5-35 | 23
20-16-9-5-35-7 | 23

## Slide 17: Coverage Issue Discussion
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38
20 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
20-16 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0
20-16-9 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0
20-16-9-5 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0
20-16-9-5-35 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
20-16-9-5-35-7 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38
6 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
6-9 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
6-9-1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
6-9-1-8 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
Even though, the combination coverage is coming to saturation, the model still could not cover all the data sets.
Some data sets show a great different than the others: e.g. data sets Nr 3, 4, 10, 29, 30, etc.
 | Single Identification | C.Model 1 Series | C.Model 2 Series
3 | 1 | 0 | 0
4 | 2 | 0 | 0
10 | 1 | 0 | 0
15 | 0 | 0 | 0
28 | 0 | 0 | 0
29 | 0 | 0 | 0
30 | 0 | 0 | 0
32 | 0 | 0 | 0
33 | 0 | 0 | 0
36 | 0 | 0 | 0
38 | 0 | 0 | 0

## Slide 18: Coverage Issue Discussion
The reason could be:
System changes during the operation
Unknown parameter missing
Data Set | Nr of Coverage | Nr to be covered
2 | 0 | 3
3 | 1 | 1
4 | 0 | 2
5 | 2 | 0
9 | 1 | 3
10 | 5 | 1
11 | 1 | 12
14 | 0 | 4
15 | 6 | 0
22 | 0 | 11
28 | 3 | 1
29 | 0 | 0
30 | 7 | 0
32 | 11 | 0
33 | 1 | 0
36 | 7 | 0
38 | 2 | 0

## Slide 19: Coverage Issue Discussion
20-16-9
6-9

## Slide 20: Conclusion
The Non-linear Hammerstein-Weiner method could be used for identification of the servo-motor system
With the limited number of data sets for identification, but careful designed process, could lead to an accurate enough model for the fast industry using.
With the number of data sets increasing, the accuracy of the identified model is increasing.
The identification process with a well-covered data sets is necessary for improving the performance of the identified model
Several models are identified instead of a single model, due to the possible missing of the parameters or the system unknown changes.

## Slide 21: Thank you!