## Slide 1: UWB for micro-drones
Yanick Büchel, EE Bachelor student
Supervisors: Dr. Michele Magno, Dr. Tommaso Polonelli
Professor: Prof. Dr. Luca Benini
Integrated Systems Laboratroy
Notes: Hello everyone my name is yanick büchel and i welcome you to the presentation of my bachelor thesis «Ultra-wideband for drones».

## Slide 2: Introduction Motivation
UAVs/Drones
Why UWB for micro-drones?
  No GNSS indoors
Challenges:
  Limited power budget
  Limited payload
Notes: As an intro want to talk about the motivation for this work. So let’s get started:
When talking about micro-drones aka UAVs – Unmanned Aerial Vehicles one of the most important aspects is to know its current position such that the flight can pe planned properly.
When it comes down to indoor positioning, the problem is that Global Navigation Satellite System e.g. GPS don’t work anymore – we call this GNSS-denied environments.
For indoor positioning a very precise method is to use a motion capture system – BUT this is quite expensive
Among other solutions, UWB stands out due to it’s very precise ToF estimation at a relatively cost.
For larger drones (example picture) additional sensor technology can be added quite easily, because…
  … the additional payload is relatively small compared to overall weight of the drone
  … the power consumed by the sensor technology is also covered easily by the large batteries
However for micro-drones it is more complicated *click*
  Theres a very limited payload of a few grams
  Limited power budget
This is one of the challenges of this work

## Slide 3: Introduction Project Goals
Goals of the project:
  Development of a PCB shield implementing the DWM3000 UWB module for the Steval-Drone
  Enable indoor localization for micro-drones
Notes: With this being said, the goal of this work was the development of a PCB for the Steval-Drone by STMicroelectronics (that you can see in the picture) that implemens Decawave’s/Qorvo’s new DWM3000 UWB module.
The module enables the drone to use TWR to estimate distances to designated anchors.

## Slide 4: Background The Steval-Drone01 Kit
Drone Kit by STMicroelectronics
Open source HW and SW
3D printed frame
DC motors, rotors and battery
Smartphone App
FCU001V1 Eval board (FCU)
  STM32F4 MCU
Maximum weight: 70g
Maximum payload: 10g
NO native support for indoor localization
Reference: en.steval-drone01_getting_started_guide.pdf
Notes: Let’s briefly talk about the starting point:
We use the Steval-Drone01 drone kit by STM which is a ready-to-fly micro drone kit, whose HW and SW is open source
It includes the 3D printed frame
motors, props, battery
and most importantly: the flight control unit which has an STM32F4 MCU as the main processing unit
8.5 x 20mm tiny electric motors
Battery: 3.7v 500mA

## Slide 5: Background FCU001V1 Flight Controller
Reference: en.steval-drone01_getting_started_guide.pdf
Notes: Now let’s have a closer look at the FCU since this is the eval board that is connected to the custom PCB in the end. The FCU implements all sensors (and even more) that are used for a controlled flight.
*click* Accelerometer and Gyroscope in the inertial measurement unit
*click* magnetometer
*click* pressure sensor
*click* a bluetooth low enery module that allows to control the drone via smartphone or tablet
*click* an integrated battery charger
*click* Lod dropout voltage regulator
Last but no least 4 power mosfets to drive the motors.
(And of course the ST32 MCU.  all included on one board!)

## Slide 6
Background QORVO DWM3000
UWB module by Qorvo
  DW3110 RF transceiver IC
  Frequency error: below 2 ppm
  On-board ceramic chip-antenna
  IEEE 802.15.-2015 and IEEE 802.15.4z
  CH5 6.5GHz/CH9 8Ghz
6/14/2021
Yanick Büchel
6
Applications
  Precision real time location systems (RTLS) using two-way ranging (TWR) or TDoA schemes in a variety of markets
  Wireless sensor networks for location awareness (WSNs)
Notes: Now as we have seen the FCU, let’s see the UWB module we want to connect it with.
It’s the new DWM3000, the successor of the DWM1000 which has already been used for quite some projects at PBL.
It has the same dimensions as the 1000 model.
The real changes took place under the hood:
Based on DW3110: low-power, single chip CMOS RF transceiver IC
Transceiver IC has Lowered power consumption
Addition of Channel 9 support
Its main applications are real time locating of assets using twr or tdoa AND parts of wireless sensor networks
Low frequency error  necessary for the exact timestamping  see next slide
6

## Slide 7: Background Double-sided TWR
Device A
Device B
Tf
TreplyA
TreplyB
Tf
Tf
Time of Flight Tf is needed for distance estimation
TroundA
TroundB
Tf
Notes: How can this sensor estimate a distance?
It estimates the the time of fligth (T_f) it took a radio wave to travel between two objects.
Because then we can use the formula on the left.
*click*
The TWR exchange goes as follows: *click*
A sends a poll message and sets a timestamp.
Upon reception of the message at B, B sets a timestamp too. *click*
As device B is computing a response, it embeds the timestamp of reception and planned transmission into it. The response is then sent. *click*
A can now calculate the time of flight as depicted in the equation on the left.
As the clocks are
Because the clocks drift slightly from each other, there is always an error in the measurement.
this simple method is therefore extended by so-called double-sided TWR.
This is to minimize the error due to the frequency drift.
The final formula is now this one on the left.
The double-sided-TWR estimates the time of flight as follows:
*click*
*click* *click*
In short: *click*
Roundtrip times are measured, they simply are the time it took from the initial transmission until the reception of the response. The response has the information about the response delay encoded such that the time of flight can be computed.
Whenever A or B receive or send a message, a timestamp is set which is passed on. *CLICK*
At the end of an exchange, the round trip times of and the response delays of A and B can be calculated. *click* With this information it is possible to estimate the time of flight with the following formula.
The green and blue lines show the time lines of two modules that perform the TWR exchange. *click*
First: Device A sends a poll message and sets a timestamps with Ttxa, then B timestamps with Trxb when receiving and adds another timestamp when transmitting Ttxb
A now has the whole rountrip time: Trxa – Ttxa = TroundA . With the last transmission from A  ‘final’ message contains previous two timestamps, namely timestamps from poll tx and response rx and also the timestamp of final tx.
*click*
While b itself has timestamped the time of repsonse tx and of final reception. B has all timestamps and thus can calculate reply times and roundtrip times.
From that, the ToF can be estimated with following formula:

## Slide 8: PCB Design High level block diagram
Notes: Now that we have seen the working principle of the transceiver, I want to talk about the actual PCB design.
Here’s a high level system overview:
On the left the flight controller connected to the custom PCB on the right.
As you can see, it powers an SPI interface for connectivity and also has an interrupt line and a reset line to reset the DW IC.
The battery voltage is connected to an on-board voltage regulator which supplies the DWM3000 with a constant 3.3 V.
Additionally, there’s an On/off line to bring the regulator into shutdown mode.

## Slide 9: PCB Design Required Signals
SPI Interface
  Chip-select (DW_NSS)
  Clock
  MOSI
  MISO
Interrupt
Reset
ON/OFF
VDD
GND
Notes: Now let’s jump to the signals in detail: *click*
For the spi interface, clock and chip select was easy available *click*
However for the MOSI and MISO the only option I found was to remove the two LEDs as you can see here
*click*
The interrup, reset and on/off line were mapped to the pins marked in green
And finally, the supply voltage and GND wasn’t that restricted and i chose the pins marked in pink.

## Slide 10: PCB Design Design Rules
Material: standard FR-4
Min. hole diameter: 0.30 mm
Min. electrical clearances: 0.15 mm
Min. annular ring: 0.15 mm
Track widths: 0.15 mm 0.30 mm (GND and VDD)
Overall thickness: 0.80 mm
Layers: 2, double-sided
Notes: The design was done in Altium Designer (see schematic on the right)
Material FR-4 (flame retardant)
Rules kept standard to keep cost low with…
… min holes of 0.3mm
… min. el. clearances
…min annular rings
… and min. track widhts of 0.15 mm  here i used 0.3mm for GND and VDD to reduce resistance.
The only aspect that’s a little of standard is the thickness of 0.8 mm instead of common 1.6 mm
2 layers, mounted components on both sides

## Slide 11: PCB Design Components
Passive
  Current limiting
  Bypass capacitors
  Smooth out transients from sharp edges
Acitve
  LEDs
  LDO
Notes: Ldo: low noise because no switching
Current is quite low such that the efficiency doesn’t suffer too much
if vin is not a lot higher than vout  good efficiency
LED for debug and/or as RXLed and TXLed
With the low dropout voltage < 100 mV the battery’s capacity can be used to higher percentage  healthier for battery if not discharged completely to 3.0 V

## Slide 12: Software Flow Chart TWR Initiator
Notes: -To test the pcb shield, a software implementing double-sided TWR was written.
-It is based on the API guide for the DWM3000 and is modified such that it runs on the Flight control unit of the drone.
-this firmware was tested successfully and proved to be working.
This twr code is ready to be merged with the flight control firmware from STM such that TWR is performed while flying
The software flow goes as follows:
After both the fcu and dwm3000 have started up, the dwm checks it’s calibration and is then ready for the TWR scheme:
It sends a poll, waits a certain time for a response and if timeout time isnt exceeded upon reception; then it sends the final message

## Slide 13: Results The DWM3000 Shield
Mounted onto the drone frame
Dimensions of the PCB Shield
Weight: ~3 g
Notes: Left picture planning with 3D model and actual outcome
Right the dimensions and weight

## Slide 14: Results Power Consumption
Time for one measurement: 2 ms
Peaks: 150 mW (TX), 187 mW (RX)
Average power: 78.6 mW
48.7 mW in between TWR exchanges
Decrease further with shutting down the system
Chart: Estimated power consumption
| 10 | 20 | 50 | 100 | 150 | 200 | 400
average power | 49.3 | 49.9 | 51.69 | 54.68 | 57.67 | 60.66 | 72.62
Poll (tx)
Response (rx)
Final (tx)
Notes: TX | RX | TX <-> poll, response, final
150 mW for poll and final
Whereas reception of the repsonse around 187 mW
Between frames 48 mW
Average: 78.6 mW
Time period: 2 ms
Note: in software the time between frames can be changed (out of this work’s scope)
calculated how much power is consumed when ranging frequency is changed
See right graph: from 10 Hz at 49.3 mW it increases linearly to 400 Hz at 72.6 mW average

## Slide 15: Results DWM3000 Shield Specs
To all pins apply max. 3.6 V (except the ON/OFF of the LDO)
Parameter | Min. | Typ. | Max. | Unit | Note
Supply Voltage | 3.3 | 3.3 – 4.2 | 6 | V | Typically in the LiPo/Li-Ion range
Supply Current (IDLE at 4.2V) |  | 12 |  | mA | At 4.2 V
Supply Current (Shutdown mode) |  | 1 |  | nA | 
TX |  | 40 |  | mA | At 3.7 V
RX |  | 50 |  | mA | At 3.8 V
Logic Level |  | 3.3 |  | V | 
Notes: Finally, here is a table that show the electrical specifications:
Note here that a transmission draws less current than a reception which is also coherent with the datasheet of the DWM which states that reception is more power hungry.
The input voltage range is typically the one of a LiPo/Li-Ion battery
The maximum supply current is limited by the LDO at 300 mA (always well below)
In shutdown mode it was not possible to measure with the multimeter  in fact it’s 1 nA (datasheet)
At around 3.7 V the current during a TX is 40 mA and during RX 50 mA
The logic level of the PCB is at 3.3V

## Slide 16: Conclusions and future work
Conclusion:
Developed a custom PCB for the Steval-Drone
Written a firmware for the FCU to perform TWR
Can now integrate the DWM3000 in the system
Future outlook:
Perform TWR measurements while flying
Development of a system for positioning of the drone
Notes: Mention the that one of the engineers that developed this platform is interested in this project and mentioned to tommaso that it might be a candidate for a fair a twhich STM is in rome this fall (nothing official yet)