## Slide 1: Comparison of state of charge estimation methods based on Artificial Intelligence algorithms for lithium-ion batteries used in automotive applications
Master Degree in AUTOMOTIVE ENGINEERING
Master Degree Thesis
Supervisors:
Candidate:
Prof. Angelo Bonfitto
Ing. Sara Luciani
Zhang Mingyuan

## Slide 2: Outline
Introduction
Step 1: SOC estimation Network comparison
Step 2: SOC estimation considering SOH
Step 3: SOC-SOH combination estimation system
Conclusion

## Slide 3: Introduction
SOC: The available energy remaining in the battery pack.
Coulomb counting equation:
Range anxiety is common among a large number of BEV drivers.
SOC cannot be measured directly.
Find a fast, simple way to get the precise SOC
A real-time estimation system for both SOC and SOH
Object:

## Slide 4
State-of-the-art methods:
Coulomb counting
Open circuit voltage
Kalman filter
AI
Pros:
Simple
Reliable in a short period of time
Cons:
Cumulative error
Neglect aging phenomenon
Pros:
Simple
Cons:
The battery needs to stand for a long time
Neglect aging phenomenon
Pros:
Considering battery aging
Relatively precise
Cons:
Computational heavy
The accuracy strongly rely on the battery equivalent model
Pros:
Optimal for non-linear problems
Avoid complicated battery model or reactions
Considering battery aging

## Slide 5: Step 1: SOC estimation Network comparison
In this step, dataset from [1] has been used as first attempt.
[1]Carlo Vidal: ”Estimating battery state of charge using recurrent and non-recurrent neural networks”.
Focusing on the performance of three different neural networks:
FNN--LSTM--NARX
After comprising, choose one of the three in order to get into the next step.

## Slide 6
Networks’ schematics
LSTM
NARX
FNN

## Slide 7: Dataset measurement and introduction

## Slide 8
Training and Testing

## Slide 9: Results comparison
Chart: Single training time comparison (3000epochs and 5 inputs)
| FNN(DL) | LSTM | FNN(ML) | NARX
TIME(3000epochs and 5 inputs) | 680 | 2700 | 3000 | 980
Chart: RMSE% final comparison (3000epochs and 5 inputs)
| NARX | FNN(ML) | FNN(DL) | LSTM
5 inputs RMSE on test 3 (25 degree) | 0.21 | 0.357 | 1.434 | 1.089
5 inputs RMSE on test 11 (-10 degree) | 0.233 | 1.501 | 2.363 | 1.989
RMSE_mean | 0.299 | 1.125 | 2.631 | 2.237
Best performance!

## Slide 10
Step 2: SOC estimation considering SOH
In the second step, a new dataset measured by LIM is used for the second attempt, which consists of many different working phases.
The best performance network (NARX) and its structure are chosen from the previous step.
The battery we used for sampling data

## Slide 11
Battery test plan details
Training data
Testing data
Dataset measurement and introduction
Cycle start

## Slide 12
Best solution :
Training with
1° battery :
Testing with
3° battery :

## Slide 13
Training and Testing
Training data
Testing data
Take the best NARX
New battery
Configure the best NARX
Best NARX configuration:
Learning rate: 0.01
Epochs:3000
Activation functions: Tanh,Purelinear
Number of neurons: 15-20
Input delay: 0:1
Feedback delay: 1
Remains the same!

## Slide 14
55 cycles divided into 3 classes:
55 cycles divided into 5 classes:
55 cycles with only one class and an additional SOH input:
Class
Chart: 
Chart: 
Results comparison
Chart: 
| Class 5 | Class 4 | Class 3 | Class 2 | Class 1
 | 0.032335 | 0.02686 | 0.028854 | 0.026505 | 0.039326
Chart: 
 | 0.031621
Chart: RMSE%
| Class 3 | Class 2 | Class 1
 | 0.029109 | 0.014019 | 0.036041
Class 1 | 1-17 Cycles | SOH: 100%~95%
Class 2 | 18-34 Cycles | SOH: 95%-90%
Class 3 | 35-55 Cycles | SOH: 90%-82%
Class 1 | 1-11 Cycles | SOH: 100%~96%
Class 2 | 12-22 Cycles | SOH: 96%-93%
Class 3 | 23-33 Cycles | SOH: 93%-90%
Class 4 | 34-44 Cycles | SOH: 90%-87%
Class 5 | 45-55 Cycles | SOH: 87%-82%
Only 1 class | 1-55 Cycles | SOH: 100%-82%

## Slide 15: Step 3: SOC-SOH combination estimation system
The networks will be extract from Matlab code to Simulink blocks, in order to obtain a real-time system to estimate SOC and SOH at the same time.
SOH
From the concept proposed by [2], in this step, the target is to work out some details to get the system up and running.
[2]Angelo Bonfitto:”A Method for the Combined Estimation of Battery State of Charge and State of Health Based on Artificial Neural Networks”

## Slide 16
Estimation strategy
Real-time SOC
‘Input’
Real-time SOH
‘Trigger’

## Slide 17
SOC estimation system
If-action one of three subsystem
NARX-closed network

## Slide 18
Other options of SOC estimation system
5-Class NARX
Similar to schematic of 3-Class NARX, but with more if-action subsystem and 5 networks
1-Class NARX
(An additional SOH is mandatory and should be feedback from SOH estimation system)

## Slide 19
The combined system
5
3
2
1
1
4
5-Class NARX system combined with SOH system
1-Class NARX system combined with SOH system
3-Class NARX system combined with SOH system

## Slide 20
Some results
SOH Results
SOC Results

## Slide 21
Results comparison
Chart: 
| 3-Class | 5-Class | 1-Class
Time for estimating 52 cycles | 156 | 170 | 35
Chart: Combination system results
| 3-Class | 5-Class | 1-Class
SOC-Charging RMSE%_mean | 0.87 | 1.12 | 9.86
SOH-Charging-RMSE% | 1.99 | 3.65 | 44.98
SOC-PRW-Disharging RMSE%_mean | 2.63 | 3.48 | 6.36
Best performance!

## Slide 22: Conclusion
A high performance network for estimating SOC is obtained.
Through this network, a real-time, lightweight system is built up.
Narx and LSTM networks are combined, SOC and SOH can be estimated at the same time.
Considered charging-discharging，real-driving application.

## Slide 23
Thanks for all!

## Slide 24: SOH estimation system
Overall system
Feature extraction subsystem
Network subsystem