## Slide 1: LDPC 5G decoder implementation for EMBB project
Author: Riccardo Torres
Supervisor PoliTo: Maurizio Martina
Supervisor EURECOM: Renaud Pacalet

## Slide 2: Overview of the library to be implemented
The grey blocks will not be implemented in this Project.
The two green blocks are used for handling the transfer of data inside and outside the library.
The red block is used for processing the decoding process.

## Slide 3: INTRODUCTION TO THE TOPICS COVERED
The discussion of this block will be divided into the following parts:
  Overview of general block structure
  Analysis of the most important blocks
  Generation of control signals
  Timing diagram using the processing of the first two lines as an example.

## Slide 4: Process Sub System (PSS)
This block deals with decoding, and its structure is divided into three blocks:
  ROM: where the PSS control signals are stored. The values stored in this block are actually stored in the MSS.
  PRAM: where the samples to be decoded are stored.
  PE: where the decoding algorithm is processed.

## Slide 5: PROCESSING ELEMENT (PE)
The structure of this block is intended to implement algorithm 5 shown in the figure.
The algorithm in question is the result of various optimizations; it divides the decoding work into two phases:
  The first phase runs from line 7 to line 25; it takes care of updating vectors' value, previously initialized in line 9.
  During the second phase, the new corrected values of the samples (next_gamma) will be generated. This correction is made using the array of values previously updated during the first phase.
As the LDPC algorithm is iterative, it is necessary to save the array values calculated in the first step to be reused for subsequent iterations.
The R_RAM memory is used to store the arrays of values calculated during the first phase, then read during subsequent iterations.

## Slide 6: GRAM
This memory is used for storing values, as in the second one, the previously analyzed gamma values must also be used to generate the correct values.
For this reason, a single-access memory is used within the project. Its use, however, makes it necessary to have clock strokes in which no phase is processed, and the memory is accessed in reading mode for the second phase.
To eliminate this problem and guarantee independence between the first and second phase, this memory is replaced by a dual-port memory.

## Slide 7: Parallelisation of the two phases
Finally, what is missing actually to process the two phases in parallel is to ensure that the array of values calculated during the first phase is stored, as needed during the second phase.
For this reason, the register G_NEW was introduced, which is identical to R_NEW, but unlike it, its value is only updated at the end of the first phase in order to store the new value array.

## Slide 8: PE Timing diagram
The timing diagram opposite summarises all the features discussed above.
Following the workflow, it is interesting to note the following points:
  The constant use of both GRAM read and write operations.
  The alternation of RRAM read and write operations.
  The updating of the G_NEW_REG values at the end of the first phase.

## Slide 9: PRAM
This block handles the management of new and old gamma values sent and received, respectively from the PE.
Its initial structure, shown in the image above, is already equipped with two barrel shifters for the rotation of the values to be analyzed. This is because, to parallel the first and second phases, it will also be necessary to manage in parallel the data to be sent and those to be rewritten in GBIGRAM.
In this case, the only optimization is implementing a bypass process that allows the data coming from a previous PE processing to be analyzed directly without the need to rewrite them in memory.

## Slide 10: Control signals generator
The last of the three blocks is the ROM and what is interesting is not the hardware implementation but the software implementation that leads to the generation of the signals that will then be stored inside the ROM.
For this purpose, Python code was written to describe the behavior of the entire datapath and simulate data movement within it.
For this purpose, values can be set at program launch to set the memory elements within the circuit, leading to a delay in propagating the data.
In this case, the two memory elements register at the input of the PE and the GBIGRAM.

## Slide 11
LDPC Base graph and its parity check matrices
These parameters define which values are to be analyzed for decoding.
In particular, depending on the lifting size value chosen, it is possible to extrapolate the rotation value associated with each column.
In this case, the value z = 384 was chosen, which corresponds to the maximum potential rotation value.
This value falls within the second set and therefore, the values used will be those of the second column (set index = 1).

## Slide 12: It is important to note that analyzing the rows in the order described by the base graph leads to situations where, when moving from one row to another, there is a significant difference in the number of columns analyzed. This means that it will be necessary to stop one of the two phases in many cases because it is waiting for the other to finish. This problem is solved by reordering the rows at the beginning of the process.

## Slide 13
In addition to reordering rows, it is also possible to reorder columns.
This optimization stems from the observation that two successive rows often have columns to process in common. For this reason, a bypass option has been added.
To take full advantage of this feature, it is necessary first to process the second phase within the PE, relating to the columns that are also present in the next row.
However, this reordering of addresses inevitably affects the index's choice for the first phase. It can no longer be chosen simply by increasing its value each time but must be congruent with that used for the second phase. In this way, the unread gamma values will not be overwritten.

## Slide 14
A final consideration should be made when it is necessary or optional to pipeline the barrel shifter.
In this case, it will be necessary to implement a chip enable to block the data rotation process during the bypass period.
Without a chip enable, all the data inside the barrel shifter would inevitably be lost during the bypass period, as can be seen in the table on the left.

## Slide 15
PE Timing Diagarm
This timing diagram shows PE processing in the case of the two rows of the base graph.
The values highlighted in yellow represent the columns present in both rows.
The values highlighted in orange represent the rotation value associated with each column.

## Slide 16
PRAM Timing Diagram

## Slide 17: QUESTIONS?

## Slide 18: THANK YOU FOR YOUR ATTENTION