## Slide 1: Vehicle Performance Simulations with
In collaboration with
Prof. Federico Millo
Marcello Rimondi
Paolo Ferreri
Project Update 11/10/2022
André Fernandes
Notes: Welcome
DO NOT READ SLIDES More Info than Necessary
Follow highlights!

## Slide 2: On Today’s Menu:
Discuss Thesis Objectives
Explore Modelicas’ Simulation Environment
Case Studies:
  Backwards Battery/FC Hybrid Model
  Forwards BEV Model
Project Status
Preliminary Conclusions

## Slide 3: Objectives
Build a software package – with OpenModelica – capable to evaluate:
  Vehicle Performance Indexes.
  Range/Fuel Economy.
Compare Results with the ones obtained by commercial software.
Evaluate portability of such models.

## Slide 4: What has been done thus far?
6 things:
  Learn the Modelica Interface & Classes.
  Exploration of other projects & Libraries.
  Test Modelica Standard Library (MSL4.0).
  Creation of Simple Backwards Hybrid Model.
  Construction of Custom Library for Future Models.
  Creation of Simple Forward BEV Model.
Currently not in use; however useful & free. Some Libraries contain useful prebuilt models which can save the user time and effort. However, sometimes not updated and compatible with MSL 4.0

## Slide 5: So where are the struggles?
(1) OMEdit tutorials are either very basic or very complex.
  Learning via:
    Discussing with colleagues.
    Example models.
    Trial and error.
(2) OMEdit is NOT intuitive or user friendly.
  Objects often do not behave as expected.
  No detailed support website like with MathWorks.
(3) OMEdit is very slow… everywhere…
  If models become overly complex, clicks take time to register.
    Necessary to make models within models to solve this issue.
  Simulations take several minutes to complete…
Notes: (1) Tutorials (2) Error Messages not friendly
(3) Slow

## Slide 6: On Today’s Menu:
Discuss Thesis Objectives
Explore Modelicas’ Simulation Environment
Case Studies:
  Backwards Battery/FC Hybrid Model
  Forwards BEV Model
Project Status
Preliminary Conclusions
Notes: A programming language by Modelica Association

## Slide 7: How to use OpenModelica? → OMEdit!
Two ways to model:
  Graphically, similarly to Simulink, Simscape, Labview, etc.
    Signals, like in Simulink, are unitless and interact with Mathematical Blocks.
    Connections, like in Simscape, carry “Power” via Force & Displacement, or Torque and Angle, or Current and Voltage, etc.
  Programming in Modelica Language
    One section for declaring variables.
    One section for declaring equations.
    One section for creating algorithmic structures.
Another Feature:
  Model/Package drawing & graphics (Buggy)
Notes: (0) Graphical vs Text Programming
Algorithms make even slower (1) Custom Icons

## Slide 8: Modelica Classes
Package
  Groups together other classes & properties.
  Works similarly to a folder.
Model
  An entity that can be simulated.
  Can be made of other models.
Block
  A component of a model that requires inputs to be simulated. ie; Can not be simulated by itself.
Type
  Creation of unique (custom) data types.
Class
  For text documents. Contact, Release version, etc.
& Options
Partial
  An incomplete component of a class. Useful for having global components that can be easily imported into other classes (such as graphical icons or variables).
Save in One File
  Saves the class as one giant ASCII text file. It is the default and NOT recommended as it tends to make modifying large models very slow.
Notes: Only first Three!

## Slide 9: The OMEdit interface:
The welcome page:
Standard Libraries.
(including MSL4.0)
User Models & Libraries.
Welcome Tab Selected
MSL 4.0
Notes: (0) Welcome Tab
Recent Files
Bakeka for News
Modelica Libraries
MSL4.0
Your Libraries & Models

## Slide 10: The OMEdit interface:
The modeling (via graphics) page:
Modeling Tab Selected
Modeling via graphics
Generic Model symbol.
Insert components
Generic Package symbol.
Custom graphic.
Notes: Generic Symbols
Custom Graphics

## Slide 11: The OMEdit interface:
The modeling (via programming) page:
Via ModelicaLanguage
Modeling Tab Selected
Simulations & Compilation verifications done from here.
Text manually written: Global parameters with default values or equations. Addition of “partials”, etc
Text appears automatically: due to graphical programming.
Notes: (1) How Text Appears

## Slide 12: The OMEdit interface:
The modeling (personalized graphics) page:
Modeling Tab Selected
Possibility to draw personalized icons in the graphical modeling page or in the model graphic page.
Also possible to import drawings from elsewhere in the file as a “partial”.
Note that the white frame should always encompass both the model and the graphic to ensure the correct hitbox of the models. One of the first bugs that was encountered is that when adjusting the white frame, either manually or automatically, the hitbox gets incorrectly set to outside the image, despite the frame being correctly positioned on the graphic.
Drawing & writing tools.
Notes: (1) Errors

## Slide 13: The OMEdit interface:
The simulation page:
Simulation Results
Values evaluated & constants, all plottable!
Errors appear here!
List of ALL equations if mis-defined system.
Error code.
Chattering.
Plots appear here… currently displaying WLTC of a typical EU passenger vehicle
Notes: Error Messages
Plot Window
Variables

## Slide 14: The OMEdit interface:
The de-bug page:
The model that is being simulated
Debug Tab Selected
Notes: (1) Model Being Simulated

## Slide 15: What do MSL4.0 Components look like?
Components from Blocks Library
Components from Mechanics Library
Components from Electrical Library
Signal Blocks
Physical Blocks
Notes: (0) Example of MSL Libraries
NOTE THE COLORS (DkBlue, Blue, Pink, Green, Gray)
Signal or Physical Libraries
Interactions (note all blocks have them)
Sensors
Sources
Physical Components

## Slide 16: On Today’s Menu:
Discuss Thesis Objectives
Explore Modelicas’ Simulation Environment
Case Studies:
  Backwards Battery/FC Hybrid Model
  Forwards BEV Model
Project Status
Preliminary Conclusions

## Slide 17: “AndrePack01” – The Original Failure
Notes: (0) Backwards Model both Speed and Force controlled
(1) Inside Vehicle

## Slide 18: “AndrePack07” - BEV
Note no slope… the goal was to obtain a working model & not to complicate!
Notes: (1) Inside Models

## Slide 19: “AndrePack07” - Hybrid
eCMS
Notes: (1) eCMS

## Slide 20: On Today’s Menu:
Discuss Thesis Objectives
Explore Modelicas’ Simulation Environment
Case Studies:
  Backwards Battery/FC Hybrid Model
  Forwards BEV Model
Project Status
Preliminary Conclusions
Notes: Scrapped Backwards Model

## Slide 21: “AndrePack11_V3”
Notes: (1) Inside Models, Physical and Signal

## Slide 22: The Current Library Structure
User Guide (Package)
  Contact (Class)
Examples
  BEV (Model)
Controllers (Package)
  Components (Package)
    Modified PID (Block)
    Modified Ramp (Block)
  Max Verstappen (Model)
  Ayrton Senna (Model)
  Unused Drivers (Package)
Speed Cycles (Package)
  Speed & Inclination Cycles (Models)
Energy Storage (Package)
  Battery Pack (Model)
  Hydrogen Fuel Cell (Model)
…
Electronics
  Inverter with PWM (Model)
  Hybridization Unit (Model)
  Motor Control Unit (Model)
Icons (Package)
  Speed Cycles (Partial Model)
  Controllers Package (Partial Package)
  Etc.
In development
In development
Notes: (0) Current Software Package
(1) In Development

## Slide 23: Overview of The Model
6 Models
Battery Model
(BatteryPack_V02)
Speed Cycle
Motor & Inverter
(SMPM_Motor_V04)
Chassis (Bus)
(SimplifiedLongitudinalDynamics_NoSlip)
Driver
(AyrtonSenna)
Motor Control Unit
(MotorControlUnit_V00)
Notes: (0) Overview
(1) 6 models

## Slide 24: Overview of The Model
All Data Signals are sent to the Global Bus for analysis!
Featuring Internal Bus
Conventional Current Direction
Current flows from the Battery to the Inverter & Motor during Traction Conditions
Torque line connects the motor and the vehicle (Bus)
Torque Transmission
Notes: (0) Data bus avoid mess (feat Internal Bit)
Electrical Line
Torque Line

## Slide 25: Overview of The Model
Data is inserted via menus of the individual Models*
*Except when tables are involved, where data must by opening the sub-models themselves
Notes: (0) Parameter input

## Slide 26: Custom Blocks/Functions
The ramp block is now time independent and controlled via a Boolean. It activated whenever the switch from False to True occurs and can now be activated several times per simulation.
The integral error can now be reset upon the application of a Boolean signal. Useful in the braking PID where every brake application should be independent of previous braking experiences.

## Slide 27: BEV: The Battery Model
3 parts: 1 physical & 2 computations
Temperature is set by the thermal port.
(Not Implemented)
Current flows to and from the external connections along the blue path.
Notes: (0) Battery Model
3 parts
Temperature
Current

## Slide 28: BEV: The Battery Model
Chart: LG18650MH1 Cells
(1) The Series Modules are MSL4.0 batteries consisting of Ns series cells and Np parallel units. Internal Resistance is independent of SOC, whilst OCV is not.
(2) Parameters are fed to the Series Modules via the Cell Data table.
(3) A current sensor (ammeter) is used to evaluate the SOC of the battery pack.
(4) Due to MSL4.0’s Batteries SOC independence for the equivalent resistance, they are all set to zero and a single equivalent resistance is evaluated for the whole battery pack.
(5) A voltmeter provides the OCV to the bus for use in other calculations.
(6) Evaluate max discharge power and recharge power the battery pack can accept. These calc. for motor management.
Notes: (0) Follow Blue Circles (1) Battery Cells
(2) Parameters
(3) Ammeter
(4) Eq. Resistance
(5) Voltmeter
(6) Max Powers

## Slide 29: BEV: The Motor/Inverter Model (Via Efficiency Maps)
3 parts: 2 physical & 1 computations
Data Bus!
Current flows to and from the external connections along the blue path. A controllable current source imposes the value.
Torque flow. A Torque source imposes a value
Battery Power request is converted into a current request.
Throttle pedal position is converted into a torque request from Motor
Notes: (0) Overview
3 parts
Internal Data Bus
Torque
Current
Throttle2Torque
Power2Current

## Slide 30: BEV: Motor Control Unit …replaced with HybridControlUnit if FC-Hybrid
If in Traction Conditions:
Torque request multiplied by motor speed to determine power request.
Power request compared to what the battery can supply.
The minimum of both values (absolute value) is selected and transmitted to the motor as a torque request, and to the battery as a current request.
If in Regen Conditions:
An approximately constant torque is applied according to the setting selected.
This value is compared to the battery limits to ensure battery limits are respected.
The maximum of both values is selected and transmitted to the motor as a torque request, and to the battery as a current request.
Notes: (0) Overview
Traction
Regen

## Slide 31: Why the mess? After all… Modelica does have plenty of electric Motor Models in their Electrical Library… Even complex & detailed ones!
Induction Motor w/ Slip Ring
Surface Mounted Permanent Magnet
Note that they are entirely physical models!

## Slide 32: Why the mess?
PUNCH|Torino is neither an electric motor, nor an inverter producer. It does not know the inductances, resistances, etc. inside each component.
It is provided solely with an efficiency map (here combined for viewing convenience) & Torque limit curves (omitted).
This map + torque limit curves are, however, insufficient as data inputs for the motor model we are about to see. It must first be run through a MATLAB script.
In case of large accelerations, the motor is limited by how much current the battery can provide. Inversely so, in case of regenerative braking. As no data is known about the electronics & motor, it is not possible to directly convert the current capable of being provided by the battery into torque for the motor.
& all of this is done through MATLAB since Modelica is more or less incapable of managing data structures!
(loaded large data structures make the software unbearably slow)
Notes: (0) Eff Maps (1) Insufficient Require Conversion
(2) Battery Impose Limits
(3) Modelica Matrix Issues

## Slide 33: Why the mess?
Convert!
A MATLAB Script multiplies together the efficiency points of the Motor & Inverter. Mechanical Power is evaluated as a product of torque and angular speed. Electrical power is evaluated as the product of mechanical power and the combined efficiency.
This structure is then re-arranged into a new map where Electrical Power and Motor Speed are the inputs & mechanical torque is the output.
Notes: (0) Non Symmetric Conversion
(1) Within Limits

## Slide 34: BEV: The Inverter – UNUSED!
Graphical Symbol of the n-phase Full Bridge Inverter
Injection of third harmonic to increase the linear region and the modulation factor.
Modelica’s n-phase Full Bridge Inverter
Despite not being used in the model, an inverter was originally created for use with the Modelica motors.
Its structure is based on Modelicas own inverter with a third harmonic injection.
Notes: (0) Unsused Inverted
3rd Harmonic Injection
Modelica Inverter

## Slide 35: BEV: The Vehicle Model without Slip
No Slip = Simplified Model -> Lump both axels and brakes together.
Torque flow
Force flow
User defined calculations
Notes: (0) Overview
No Slip Lump Axels
Force and Torque Flow
Equations: Varying tire coeff

## Slide 36: BEV: The Vehicle Model with some Slip
The slip acting on the driving wheels is evaluated by determining what traction force is necessary to balance the traction torque. The slip is then multiplied by the vehicle velocity and the resulting slip speed is applied to the contact patch. The slip evaluated using this method can be compared to the analytical calculation of slip above it to ensure it is resulting in the correct behavior of the model. As the driving axel and the non driving axel(s) experience different torques, they must be split into two components. Note that in this model, the slip is not being evaluated.
Notes: Diff methods of Slip
No Brakes
Axels Split
Old Model

## Slide 37: The Driver Model
Several driver models with different control logics were made for the forward model. Each iteration aimed to resolve new issues. The latest driver model has been nicknamed “Ayrton Senna”. Each driver model behaves differently and has different limitations.
  Ayrton Senna struggles if the regenerative braking is too high.
  Ayrton Senna typically does not follow the braking curves immediately (as he reacts to exceeding a threshold).
  Ayrton Senna typically brakes several times per braking instance.
  Small instances of Chattering.
Notes: Naming of drivers. Ayrtons issues.

## Slide 38: The Driver Model
Throttle Logic:
  If the vehicle reference speed is positive, and the reference acceleration is superior to a threshold acceleration, the driver should be on the throttle (Boolean).
  If the aforementioned Boolean is false, the throttle position is null.
  If the OnThrottle Boolean is true, a PID controller acts on the speed error between the real vehicle speed and the reference speed.
  The PID signal is divided by the maximum torque the motor is capable of supplying at the current angular speed.
  If the vehicle is going uphill, the accelerator is increased by a certain factor multiplied by the slope. If downhill, reduced by another factor.

## Slide 39: The Driver Model
Brake Logic:
  If the vehicle is meant to be stopped & OnThrottle Boolean is false, slowly apply brake pressure with a ramp signal until the brake pedal is fully compressed.
  If the difference between the vehicle speed and the reference speed surpasses a threshold value, and the OnThrottle Boolean is false, slowly apply a brake pressure determined by a PID controller. This signal is reset at the beginning of each application.
  If going downhill, increase reference brake pressure by a certain ratio.
  If going uphill, decrease reference brake pressure by a certain ratio.

## Slide 40: The Driver Model
Regen Logic:
  If the OnThrottle Boolean is off, and the vehicle speed is positive, induce Regen via a ramp signal until a pre-selected intensity.
  If the brakes are activated, increase regen via a ramp signal to a desired intensity.

## Slide 41: The Driver Model
Error Tracking:
  Error1: Total Absolute Distance Error: Integral in time of the speed error.
  Error2: Total Absolute Distance Error divided by time elapsed.
  Error3: Total Distance Error: Integral in time of the speed error.

## Slide 42: The Speed Cycles
Speed [m/s] & Inclination [%]
SORT1 (vmax = 40 km/h, imax = 0% & tend = 940s)
SORT2 (vmax = 50 km/h, imax = 0% & tend = 740s)
SORT3 (vmax = 60 km/h, imax = 0% & tend = 415s)
Braunschweig (vmax = 46 km/h, imax = 0%, d ≈ 10.87km & tend = 1740s)
MLTB (vmax = 48.71 km/h, imax = 0%, d ≈ 9.00 km & tend = 2281s)
Gillingham (vmax = 59.86 km/h, imax = 9.64%, imin = - 8.79%, d ≈ 16.59km & tend = 2875s)
Bonus Cycle: Gillingham (x3)
SORT 1
SORT 3
(Old) MLTB
Gillingham
SORT 2
Braunschweig
Artificial Cycles
Notes: (0) 6 Cycles
(1) Some artificial

## Slide 43: The Speed Cycles
Inclination Table
Speed Table
Tolerance Margin
Notes: These speed cycles are implemented in Modelica via simple time interpolation tables.

## Slide 44: How to Calibrate? Spreadsheet to track errors…
Used prior to the introduction of the braking PID.
Future calibrations involve more parameters and more error tracking.

## Slide 45: SORT3 SORT2 SORT1
Tolerance Margins
Vehicle Speed
Reference Speed
Vehicle Speed [m/s]
Error1: 32.6184 m
Error2: 0.07875 m/s
Error3: 29.2458 m
Vehicle Speed [m/s]
Vehicle Speed [m/s]
Error1: 50.4227 m
Error2: 0.06813 m/s
Error3: 45.3222 m
Error1: 60.7850 m (Total Absolute Distance Error)
Error2: 0.06466 m/s (Avg Speed Error)
Error3: 54.5550 m (Total Distance Error)
59.4 kWh Battery
Test Mass = 15570 kg

## Slide 46
Braunschweig
Tolerance Margins
Vehicle Speed
Reference Speed
Throttle
Brake
SOC
Vehicle Speed [m/s]
Error1: 155.112 m (Total Absolute Distance Error)
Error2: 0.08914 m/s (Avg Speed Error)
Error3: 73.5741 m (Total Distance Error)
SOC
FC’s 59.4 kWh Battery
Test Mass (15570 kg)
No Auxiliaries!
≈1.55 kWh/km
w/ Auxiliaries.
1.24 kWh/km
≈33.5 km
Model3 Std w/ 54 kWh does 353 km
Model3 LR w/ 82 kWh does 504 km

## Slide 47
≈1.92 kWh/km
w/ Auxiliaries.
Braunschweig
Tolerance Margins
Vehicle Speed
Reference Speed
Throttle
Brake
SOC
Vehicle Speed [m/s]
Error1: 184.028 m (Total Absolute Distance Error)
Error2: 0.10576 m/s (Avg Speed Error)
Error3: 62.7009 m (Total Distance Error)
SOC
FC’s 59.4 kWh Battery
Max Mass (19000 kg)
≈25.8 km
No Auxiliaries!
1.61 kWh/km

## Slide 48
Old MLTB
Tolerance Margins
Vehicle Speed
Reference Speed
Throttle
Brake
SOC
Vehicle Speed [m/s]
Error1: 192.384 m (Total Absolute Distance Error)
Error2: 0.08434 m/s (Avg Speed Error)
Error3: 158.095 m (Total Distance Error)
SOC
FC’s 59.4 kWh Battery
Test Mass (15570 kg)
No Auxiliaries!
≈1.58 kWh/km
w/ Auxiliaries.
1.09 kWh/km
≈38.1 km

## Slide 49
≈1.93 kWh/km
w/ Auxiliaries.
Old MLTB
Tolerance Margins
Vehicle Speed
Reference Speed
Throttle
Brake
SOC
Vehicle Speed [m/s]
Error1: 200.069 m (Total Absolute Distance Error)
Error2: 0.08771 m/s (Avg Speed Error)
Error3: 178.381 m (Total Distance Error)
SOC
FC’s 59.4 kWh Battery
Max Mass (19000 kg)
≈28.9 km
1.44 kWh/km
No Auxiliaries!

## Slide 50
Gillingham
Tolerance Margins
Vehicle Speed
Reference Speed
Throttle
Brake
SOC
Vehicle Speed [m/s]
Error1: 1823.92 m (Total Absolute Distance Error)
Error2: 0.6344 m/s (Avg Speed Error)
Error3: -1128.84 m (Total Distance Error)
SOC
FC’s 59.4 kWh Battery
Test Mass (15570 kg)
No Auxiliaries!
≈2.06 kWh/km
w/ Auxiliaries.
1.73 kWh/km
≈24.0 km
Larger Starting SOC

## Slide 51
0-100 kph
SOC_0 = 80%
Vehicle Speed [m/s]
FC’s 59.4 kWh Battery
Test Mass (15570 kg)
≈42.4 s
No Auxiliaries!
Interestingly… the simulation fails because the motor has reached its maximum rotational speed.
Admittedly, rolling resistances dependence on speed has been ignored, and internal frictions are also ignored, but the implication is that the battery pack has enough power for an even higher speed!
0-30kph in 4.62s
0-60kph in 14.0s

## Slide 52
0-100 kph
SOC_0 = 80%
Vehicle Speed [m/s]
FC’s 59.4 kWh Battery
Max Mass (19000 kg)
0-30kph in 5.64s
0-60kph in 17.2s
Again… the simulation fails due to having reached the motor speed limit.
≈53.0 s
No Auxiliaries!

## Slide 53: On Today’s Menu:
Discuss Thesis Objectives
Explore Modelicas’ Simulation Environment
Case Studies:
  Backwards Battery/FC Hybrid Model
  Forwards BEV Model
Project Status
Preliminary Conclusions
Notes: So after having explained all this, where does that leave us?

## Slide 54: Objectives
Build a software package – with OpenModelica – capable to evaluate:
  Vehicle Performance Indexes.
  Range/Fuel Economy.
Compare Results with the ones obtained by commercial software.
Evaluate portability of such models.
Notes: On the topic of the first point, the library being built aims to satisfy this request. As you can probably tell, I’ve mostly focused on creating models suitable for determining the range of the vehicle and the fuel consumption of the eventual hybrid. This does not however mean that things such as the accelerations have been neglected, as such tests simply require the creation of trivial drivers that manipulate the throttle or brake.
It is however incomplete. As a next step, I intend to first finalize my BEV model, and polish it up. What do I mean by this?

## Slide 55: On Today’s Menu:
Discuss Thesis Objectives
Explore Modelicas’ Simulation Environment
Case Studies:
  Backwards Battery/FC Hybrid Model
  Forwards BEV Model
Project Status
Preliminary Conclusions
Notes: So after having explained all this, where does that leave us?

## Slide 56
Old MLTB
Tolerance Margins
Vehicle Speed
Reference Speed
Throttle
Brake
SOC
Vehicle Speed [m/s]
Error1: 192.384 m (Total Absolute Distance Error)
Error2: 0.08434 m/s (Avg Speed Error)
Error3: 158.095 m (Total Distance Error)
SOC
FC’s 59.4 kWh Battery
Running Mass (15570 kg)
No Auxiliaries!
≈1.40 kWh/km
w/ Auxiliaries.
1.09 kWh/km
≈38.1 km

## Slide 57: Preliminary Conclusions
Modelica is very powerful, but slow.
A Hybrid Fuel Cell Vehicle Model
The Fuel Cell Subsystem
…just use
Fuel Cell Vehicle Model in Simscape - File Exchange - MATLAB Central (mathworks.com)
Modelica is very versatile, but not user friendly.
Modelica is not a MATLAB substitute… It requires an intermediary such as Python or MATLAB to convert the data.
  MATLAB has a Modelica style library built-in called SimScape…