## Slide 1: Vehicle Performance Simulations with
In collaboration with
Prof. Federico Millo
Marcello Rimondi
Paolo Ferreri
Project Update 10/01/2022
André Fernandes
Notes: Welcome
DO NOT READ SLIDES More Info than Necessary
Follow highlights!

## Slide 2: On Today’s Menu:
Reminder of Thesis Objectives
Errata Corrige
Case Studies:
  Battery Model
  Fuel Cell Model
Conclusions

## Slide 3: Objectives
Build a software package – with OpenModelica – capable to evaluate:
  Vehicle Performance Indexes.
  Range/Fuel Economy.
Compare Results with the ones obtained by commercial software.
Evaluate portability of such models.

## Slide 4: Errata Corrige!
OMEdit CAN BE slow…
  If models are badly optimized.
  If the software is installed remotely.
  If the model contains large maps directly within in.
In a previous presentation, some statements were made from the experience gathered at the time. Some turned out to be true, and others not.
Slide from Previous Presentation
Notes: (1) Tutorials (2) Error Messages not friendly
(3) Slow

## Slide 5: Errata Corrige!
All the results shown in prior presentations!
The models were re-built from the ground up to be better optimized.
Construction of new models led to errors being found in old models.
New models more robust…
Notes: (1) Tutorials (2) Error Messages not friendly
(3) Slow

## Slide 6: On Today’s Menu:
Reminder of Thesis Objectives
Errata Corrige
Case Studies:
  Battery Model
  Fuel Cell Model
Conclusions

## Slide 7: Updated BEV Model
New component models same graphics.
Same connection logic.
Auxiliaries added.
Seven components.
Better Results

## Slide 8: Updated Battery Model
2 new models made, both equivalent (under certain conditions)
Externally loaded data map (partially)
No Temperature variations
Optimized power calculations
Still uses MSL4.0 cells (not ideal).
Externally loaded data map (completely)
Optional Temperature settings & calculations
Optimized power calculations
Optional RC Component

## Slide 9: Battery Model
Electrical Circuit (#1)
Electrical Circuit (#2)
Optional Thermal Circuit
User defined Calculations
Chart: LG18650MH1 Cells
Model has some preset values.
Model loads maps from external files.

## Slide 10: Updated Motor Model
External data maps.
Fewer variables.
Interpolations & calculations moved from graphical programing to text-based.
Valid also when in use in Hybrid Vehicle.

## Slide 11: Updated Motor Model
Electrical Circuit
Torque Circuit
Data Bus
Throttle pedal position is converted into a torque request in the Motor model.

## Slide 12: Updated Motor Control Unit
All calculations moved internally to text-based programming.

## Slide 13: Minor Vehicle Model Update
Both Slip & Non-Slip have been optimized (Non-slip case being shown).
System equations has been compressed. Fewer equations → Fewer variables → Faster Simulations!
Differential moved internally to vehicle model (previously in motor model due to construction constraints)

## Slide 14: Non-Slip Vehicle Model
Torque flow
Force flow
User defined calculations

## Slide 15: Slip Vehicle Model

## Slide 16: The Speed Cycles
Speed [m/s] & Inclination [%]
SORT1 (vmax = 40 km/h, imax = 0% & tend = 940s)
SORT2 (vmax = 50 km/h, imax = 0% & tend = 740s)
SORT3 (vmax = 60 km/h, imax = 0% & tend = 415s)
Braunschweig (vmax = 46 km/h, imax = 0%, d ≈ 10.87km & tend = 1740s)
MLTB (vmax = 48.71 km/h, imax = 0%, d ≈ 9.00 km & tend = 2281s)
Gillingham (vmax = 59.86 km/h, imax = 9.64%, imin = - 8.79%, d ≈ 16.59km & tend = 2875s)
Bonus Cycle: Gillingham (x3)
SORT 1
SORT 3
(Old) MLTB
Gillingham
SORT 2
Braunschweig
Artificial Cycles
Notes: (0) 6 Cycles
(1) Some artificial

## Slide 17: The Speed Cycles
New sources load the cycles from external .txt files!
Anti-bug gain of one!
Notes: (0) 6 Cycles
(1) Some artificial

## Slide 18: On Today’s Menu:
Reminder of Thesis Objectives
Errata Corrige
Case Studies:
  Battery Model
  Fuel Cell Model
Conclusions

## Slide 19: Introducing Fuel Cell Hybrid EV Model
New Section: Fuel Cell, Balance of Plant, Boost Converter
Same construction as in BEV
Different motor controller.
Series Hybrid (Order 2, Index 1).
RBC for management of Fuel Cell

## Slide 20
Modelicas’ version of StateFlow
RBC with StateGraph
5 States Represented by the White Boxes.
  FC (Initial State)
  FC Warming Up
  FC Charging at Rate LVL1 (Battery SOC Dependent)
  FC Charging at Rate LVL2 (Battery SOC Dependent)
  FC acting as a Load Follower or Average of LVL1 & LVL2
14 Transition Gates Represented by the Black Bars
  Gates can have minimum time verifications.
  Gates can be enabled or disabled.
  Gates can be open or closed.
States can only change if all three conditions permit!
*
Unless Modelica Bugs!

## Slide 21
Fuel Cell Models
Incomplete
Two fuel cell models, one basic, one more complex.
Whole fuel cell modelled by single voltage source.
Mostly done with text-based programming.
Modelled after GT-SUITE template.
Hydrogen consumption rate determined & integrated.
Similar calculations performed for O2, H2O & Air.
Can be disabled by the RBC

## Slide 22
Balance of Plant & Constant Power Auxiliaries
From Net Fuel Cell power requests, adds an extra consumption power to model the extra power the FC must supply to run the compressor…
Represents the 12V circuits power consumption for things such as lights, music, wipers, doors… etc.
Represents other consumptions such as AC / Climate control.

## Slide 23: Preliminary Conclusions
Modelica is very powerful.
A Hybrid Fuel Cell Vehicle Model
The Fuel Cell Subsystem
If you can…just use
Fuel Cell Vehicle Model in Simscape - File Exchange - MATLAB Central (mathworks.com)
Modelica is very versatile, but not user friendly.
Modelica is not a MATLAB substitute… It requires an intermediary such as Python or MATLAB to convert the data.
  MATLAB has a Modelica style library built-in called SimScape…
OpenModelica is FREE