## Slide 1: Tesi: Modeling of the seismic Response of Masonry Structure
Comparison between Code_Aster vs 3_Muri

## Slide 2: Code_Aster and Salome_Meca
Code_Aster, acronym for Analysis of Structures and Thermo-mechanics for Studies and Research that takes into account thermal effects and dynamic loading history.
Code_Aster is a FEM Mechanical Solver Engine.
can handle following types of analysis:
linear statics
non-linear statics
dynamic Analysis
Salome_Meca
SALOME is an open-source software that provides a generic platform for pre- and Post-Processing for numerical simulation
Salome-Meca is a bundle which allows to run code_aster in a single GUI.
In SALOME-MECA there is a Module of AsterStudy

## Slide 3: Code_Aster Website http://www.codeaster.org.

## Slide 4: Case Study (Town Hall of pizzoli)
2-Story Masonry Building
Location: Northwest of city of L’aquila (Abruzzo)
School Building built in 1920.
U-shaped Regular Plan with Regular openings
Total Area= 770 m2
Total Volume= 5000 m3
Roof was replaced with RC Slab and External Elevator was added later.
This building is one of network of building monitored by Seismic observatory of Structure (OSS).

## Slide 5: Code_Aster Formats ------ Doc.(U4.21.01 )
MED, ASTER, GIBI, GMSH and IDEAS
MED format is by default and advised in code_ASTER.
MED, ASTER, GMSH and IDEAS
FEM Mechanical Solver
Command File (follow python syntax)
Text file .comm

## Slide 6: Geometry Module
Its possible to model directly on Salome Meca or import the input file in .MED file from GMSH.
Modelled just centerlines of walls
Regular Openings
1074 no of Nodes
1609 no of lines
588 no of faces/Surfaces
Object browser has all the information about the Model its possible to hide/unhide any individual Node, Line or surface you want.

## Slide 7: Meshing ---(U3.01.00)
Beam Meshing
Shell Meshing
(wall and slab)
Steps of Meshing
Create Mesh
Compute mesh

## Slide 8: Aster _Study
Add a Stage 1st
1. Read A Mesh---> ‘LIRE_MAILAGE’
2. Assign a FEM---> ‘AFFE_MODELE’
3. Section Definition---> ‘AFEE_CARA_ELEM’
For Every command there is a complete Document available on website of Code_Aster.
4. Define Material-----> ‘DEFI_MATERIAU’
5. Assign Material -----> ‘AFFE_MATERIAU’

## Slide 9: 1. Reading a Mesh ----> ‘LIRE_MAILAGE’( U4.21.01 )
MED, ASTER, GIBI, GMSH and IDEAS
3 types of Checks are made:
absence of orphan nodes
absence of meshes in double
absence of too flattened meshes
INFO_MED=1: No Impression,(By Default)
INFO_MED=2 only impressions relating to the correspondence family/group,
INFO_MED= 3 the totality of information is printed
Verbosity =1 (By Default)
Verbosity=2 (Increases output data)

## Slide 10: 2. Assign a FEM---> ‘AFFE_MODELE’( U4.41.01 )
3 types of Phenomenon:
Acoustic
Mechanic
Thermic
2-Node Beam Element for Beam ----------->POU_D_T (U3.11.01)
4 Node Shell Element for wall and slab----> COQUE_AXIS (U3.12.02)

## Slide 11: 3. Section Definition---> ‘AFEE_CARA_ELEM’(U4.42.01 )
3 types of sections:
Rectangular
General
Circle
3 types :
Constant
AFFINE(if surface of section varies in a linear way between 2 section)
Homothetic(if dimension of section varies in a linear way between 2 section)

## Slide 12: 4. Define Material-----> ‘DEFI_MATERIAU’ (U4.43.01 )
There are 26 different types of materials that can be defined in aster code.
I defined 11 different types of material as shown in table above;
The operand ‘E’ is used to define the young modulus of material and its checked that value of E≥0.
The operand ‘Nu’ is used to define the poisson ratio of material and its checked that value of -1≤v≤0.5.
The operand ‘rho’ is used to define the density of material, no check on density of material is defined

## Slide 13: 5. Assign Material-----> ‘AFFE_MATERIAU’ (U4.43.01 )
Material property is assigned to either Mesh or to FEM.
Each Mesh can be affected by 1 type of material.
Its possible to give the external property to the material.
If some material property changes with time, then a keyword ‘EVOL’ must be used with that variable.

## Slide 14: 6. Load and Boundary Condition-----> ‘AFFE_CHAR_MECA’ (U4.44.01 )
U4.44.01
ALL- FIXED

## Slide 15: 7.PRE-Analysis----> ‘ASSEMBLAGE’ (U4.61.21 )
MASS AND STIFFNESS MATRIX CALCULATION

## Slide 16: 8. MODAL Analysis----> ‘CALC_MODES’ (U4.52.02 )

## Slide 17: 9. Running Analysis---> ‘CALC_MODES’ (U4.52.02 )

## Slide 18: 10. MODAL Analysis----> ‘CALC_MODES’ (U4.52.02 )
[Displacement in m]
Linear Elastic FE analysis considering gravity loads

## Slide 19
11. MODE SHAPES----> ‘CALC_MODES’ (U4.52.02 )

## Slide 20: THANKS