## Slide 1: POLITECNICO DI TORINO MSC In automotive engineering
Rapporteur: Ing. Luigi Garibaldi
Co-rapporteur: Ing. Alessandro Daga
Analysis of the metamaterials for NVH vehicle applications
Student: David Agabiti s286347
A. Y. 2022/2023

## Slide 2
Metamaterials are characterized by a frequency region called stopband leveraging on the local resonance mechanism
Composed by a host structure and a local resonator
They permit to achieve both low frequency bandgap and a compact and lightweight design
tunable characteristics
Introduction

## Slide 3: Material property analysis
It is considered the hypothesis of infinitely extended metamaterial
Starting from the equation of motion of a single unit cell, for a harmonic excitation:
(1)
Let us now consider the 1D elastic wave propagation equation in the x direction:
(2)
Considering a 1D periodic metamaterial, we can link the amplitude from the starting of the unit cell (𝑥0) to its end (𝑥1 = 𝑥0 + 𝑎) in the form:
By applying the theorem in the general formulation to equation (2), it is obtained:
(3)

## Slide 4: Nomenclature
The frequency range in which no free wave solution is found is called bandgap
In this region noise and vibration reduction is expected
The periodicity is the unit cell dimension along a given axis
UC design will be referred as Periodicity / T-element size

## Slide 5: Vibration applications
Resonator unit cell design | Resonator material | Evaluated bandgap [Hz] | Unit cell dimensions [mm]
Torsional local resonators | NA | 87-90 (3) | NA
Z-shaped frame | aluminum | 178-198 (20), 198-225 (27) | 65 x 65
T-shaped | aluminum | 615-635 (20) | 40 x 40
Hollow parallelepiped | photopolymer | 350-390 (40) | 30 x 30
Composite sandwich with spiral resonators | SCFRPs and CCFRPs | 490-600 (110) | 20 x 25
Single cantilever beam | PMMA | 490-540 (50) | 25 x 25
Cantilever beam with endpoint mass | PMMA (body), steel (endpoint mass) | 292 -323 (31) | 35 x 20
Mechanical resonator solutions

## Slide 6: Acoustics applications
Resonator unit cell design | Resonator material | performances | Unit cell dimensions [mm]
Microperforated plate | aluminum | Three sound absorption peaks at 608 Hz and 926 Hz and 1663 Hz | 60 x 60
SONOBEX Noise Trap panel | steel | 60 dB transmission loss attenuation | 200 x 200
Helmholtz resonator solutions
Mechanical resonator solutions
Resonator unit cell design | Resonator material | Evaluated bandgap [Hz] | Unit cell dimensions [mm]
Basic spring-mass resonator | NA | 445-644 (199) | 50 x 50
Two cantilever beam | polyamide | 193-224 (31) | 65 x 25

## Slide 7: Acoustics applications
Resonator unit cell design | Resonator material | Bandgap [Hz] | Unit cell dimensions [mm]
Two separated beams | martensite-hardenable steel | 227–243 (16), 243–273 (30) | 36 x 36
Single-stage multi-degree-of-freedom resonator | NA | 370-390 (20), 455-465 (10), 810-850 (40) | 30 x 30
Plate with multiple cantilever beams | NA | 32- 37 (5) | 300 x 75
Mechanical resonator solutions

## Slide 8: Developed Numerical model
The Bloch-Floquet periodic boundary conditions were applied to the relevant parallel faces of the unit cell
In these Boundary conditions, the components of the wave vector were specified
Finally, a parametric sweep of the wave vector is set

## Slide 9
For example, considering a square unit cell, the wave vector is defined in function of the arbitrary defined “ii” parameter, such as:

## Slide 10: Host structure validation
Research paper
Numerical results
No bandgap is observed

## Slide 11: T-shaped solution validation
a complete bandgap is observed for the 620 - 635 (15) Hz frequency range.
Research paper
Numerical results

## Slide 12: Unit cell design
Then, it was decided to change the aluminum local resonator design and make it completely flat with a square spacer plate, for ease of manufacturing
The obtained bandgap is narrower than the original design, that is 622-627 Hz

## Slide 13
In the new design it was removed the steel host structure and spacer plate, while the resonator was kept the same as before.
A larger bandgap is observed the with respect to the original design, between 432 – 500 Hz (68 Hz)

## Slide 14: Periodicity topology optimization
60/20 aluminum unit cell design
No complete bandgap is observed

## Slide 15: Mass addition
40/20 aluminum unit cell design with endpoint mass
Bandgap between 445 – 513 Hz (68 Hz)
Same stopband width with respect to the 40/20 original configuration but shifited towards higher frequencies

## Slide 16: T-element rescaling
40/35 aluminum unit cell design
Bandgap between 232 and 279 Hz
It has a reduced stopband width with respect to the 40/20 original configuration and it is moved towards lower frequencies

## Slide 17: Material variation
40/20 steel unit cell design
Bandgap between 445 – 513 Hz (68 Hz)
Same stopband width with respect to the previous case but shifted towards higher frequencies

## Slide 18: OVERVIEW TABLE
Unit cell design | Material | Thickness [mm] | Mass addition | Bandgap [Hz]
40/20 | Aluminum | 0,5 | no | 432-500 (68)
50/20 | Aluminum | 0,5 | no | 411-460 (49)
60/20 | Aluminum | 0,5 | no | No complete bandgap
35/20 | Aluminum | 0,5 | no | 443-517 (74)
30/20 | Aluminum | 0,5 | no | 450-537 (87)
30/15 | Aluminum | 0,5 | no | 1130-1200 (70)
40/35 | Aluminum | 0,5 | no | 232-279 (47)
40/20 | Steel | 0,5 | no | 202-269 (67)
40/20 | Aluminum | 0,5 | yes | 445-513 (68)
40/20 | Steel | 1,0 | no | 885-1020 (135)

## Slide 19: Acknowledgements
I would like to thank my rapporteurs, Ing. Luigi Garibaldi and Ing. Alessandro Daga, for providing me the thesis opportunity about this interesting and innovative topic. Their support and help, when carrying out the thesis, were really important for its success.
I would also like to thank my family and friends for their constant encouragement and belief in me not only during this period but throughout my entire university career.