## Slide 1
Noise-Aware UAS Flight Path Planning in Urban Environments with Reinforcement Learning
Presented by: Shahin Sarhan
Advisors: Prof. Stefano Primatesta
Prof. Giorgio Guglieri
Ing. Marco Rinaldi
Academic year: 2023-24

## Slide 2
  The advent of Unmanned Aerial Vehicles (UAVs) has revolutionized various sectors, including surveillance, delivery services, search & rescure and environmental monitoring.
  Urban Air Mobility (UAM) envisions using UAVs for efficient transportation of goods and passengers, reducing ground traffic congestion.
  However, noise pollution from UAVs poses significant challenges in urban environments, impacting public acceptance and regulatory compliance.
Introduction

## Slide 3
State of the Art
Path Planning Algorithms
Sampling Based
Node Based
Mathematical Model Based
Bio-inspired
Probabilistic Roadmap
Mixed-Integer Linear Programmimg
Djikstra
Particle Swarm Optimization
Machine Learning Based
Rapidly-Exploraing Random Tree
A*
Genetic Algorithms
Reinforcememnt Learning
Noise Mitigation Techniques
Trajectory Optimization
Blade and Fuselage Design Modification
Active Noise Cancellation
Noise Propagation Analysis
Ray Tracing
Gaussian Beam Tracing

## Slide 4
Methodology
  Study Area
  Noise Propagation Analysis
  Reinforcement Learning
  Noise Source Modelling
  Ray Tracing

## Slide 5
  Turin, chosen for its diverse urban architecture and different demographic settings.
  Area of Interest from 7.6039 E to 7.708 E and from 45.0386 N to 45.1069 N.
  Buildings location data sourced from OpenStreetMap (OSM).
Study Area

## Slide 6
Study Area
  Entire area represented by a 3D matrix, denoted as 𝑅(𝑖,𝑗,𝑘).
  Population density data sourced from Meta.
  Similarly, the population density map for the same region is derived.

## Slide 7
  A point-source spherical propagation model for the sound generated by the UAV was utilized.
  Assuming that the noise propagates isotropically.
  Typically, a constant noise source is assumed in such models.
  However, the velocity of the drone is correlated with its noise level.
  Since the RL agent can adapt its velocity, it is beneficial to incorporate the velocity into the noise model.
Noise Source Modelling

## Slide 8
  Sound Pressure Level (SPL) at a distance of 1 m from “DJI Inspire 2” quadrotor at velocities of 5,10,20 km/h are recorded.
(Škultéty et al, 2023)
  Measurements were taken across frequencies, ranging from 20 Hz to 20 kHz, using third-octave bands.
  For each velocity, the mean SPL across all frequencies was computed.
  An exponential curve was fit to the data points, resulting in the SPL-velocity relationship
Noise Source Modelling

## Slide 9
Noise Propagation
  Four concentric circles set around the source at ground level, each with a radius incrementally larger by 10 m and populated with points distributed equally on the circles resulting in a total of 46 rays.
  Direction vectors from the source point in the sky to each ground point were computed and normalized to unit vectors

## Slide 10
Ray Tracing
The following assumptions are made in the ray tracing model:
  Medium Homogeneity: The air through which the sound propagates is assumed to be homogeneous, with consistent properties such as temperature, atmospheric pressure and humidity.
  Linear Propagation: Sound waves are assumed to travel in straight lines unless they encounter obstacles or interfaces that cause reflection or absorption.
  Specular Reflection: Reflections off surfaces are assumed to follow the law of specular reflection. Diffuse reflections are neglected for simplicity.
  Negligible Diffraction: Diffraction effects, where sound waves bend around obstacles, are neglected for simplicity. Other more complex factors such as doppler effect are also not considered.

## Slide 11
Evaluate velocity
v = ||dx, dy|| / T
Start
Evaluate the Overal SPL:
L_tot = 10log(∑10^(Li / 10))
Evaluate Source SPL
L0 = 60.24 * exp(0.003379 * v)
For ray = 1 to N
Update Coordinates
x(t+1) = x(t) + x_dir * α
y(t+1) = y(t) + y_dir * α
z(t+1) = z(t) + z_dir * α
Ray Leaves Map Boundary?
Break
Continue
Ray Collides with Obstacle?
Evaluate distance travelled
d = ||[x(t), y(t), z(t)] - [x(t+1), y(t+1), z(t+1)]||
Update Direction Vectors (x,y,z)
x_dir​=x_dir​−2(x_dir​⋅N)⋅N
z(t+1) = 2?
Evaluate geometric divergence and atmospheric absorption attenuations:
𝐴_𝑑𝑖𝑣=20log(d)+11;
𝐴_𝑎𝑡𝑚= 𝛼d/ 1000;
Evaluate the SPL: 𝐿𝑖=𝐿0−𝐴_𝑑𝑖𝑣⁡−𝐴_𝑎𝑡𝑚
YES
NO
NO
YES
NO
YES
Ray Tracing

## Slide 12
Reinforcement Learning
  At each discrete time step, the agent receives observations and rewards from the environment and sends actions back.
  The reward provides immediate feedback on the success of the agent's previous action relative to the task goal.
  RL is typically modelled as a Markov Decision Process (MDP) consisting of (state, action, reward, resulting state).
  The objective of the agent is to maximize the expected sum of discounted future rewards G(t).
  The agent gradually updates its policy 𝜋 towards 𝜋∗ via Q-Learning or Policy Optimization methods.

## Slide 13
Policy Optimization | Q-Learning
Directly optimizes a policy π(θ) through gradient ascent. It often involves learning an approximator 𝑉𝜙⁡(𝑠) for the value function. | Learns an approximator Qθ(s,a) for the optimal action-value function Q∗(s,a).
Updates are on-policy | Updates are off-policy.
Stable, reliable, but less sample-efficient | Sample-efficient, but less stable
  State-Value Function Vπ(s): Expected return from state s following policy π.
  Action-Value Function Qπ(s,a): Expected return after taking action a in state s and following policy π.
  Optimal Q-Value Q∗(s,a): satisfies Bellman optimality equation.

## Slide 14
  The DDPG algorithm is a model-free, off-policy RL method.
  It is an actor-critic RL agent designed to concurrently learn a Q-function and a policy.
  Actor: Determines the deterministic policy 𝜋(𝑠)
  Critic: Evaluates the action-value function 𝑄(𝑆,𝐴)
  Training Process: Uses experience replay and target networks for stability.
Deep Determenistic Policy Gradient

## Slide 15
DDPG agents maintain four function approximators to estimate the policy and value
functions:
▪ Actor 𝝅(𝑺;⁡𝜽) takes observation 𝑆 and returns the corresponding action that maximizes the long-term reward.
▪ Target Actor 𝝅_𝒕(𝑺;𝜽𝒕) Periodically updated using the latest actor parameters 𝜃 to improve optimization stability.
▪ Critic 𝑸(𝑺,𝑨;𝝓⁡) Takes observation 𝑆 and action 𝐴 as inputs and returns the expected long-term reward.
▪ Target Critic 𝑸_𝒕(𝑺,𝑨;⁡𝝓𝒕) Periodically updated using the latest critic parameters 𝜙 to maintain stability.
  Since the policy is deterministic, on-policy exploration at the start may not cover a sufficiently diverse range of actions to obtain useful learning signals.
  To enhance exploration, Ornstein-Uhlenbeck noise is added to actions during training.

## Slide 16
  Actor, critic, and their target networks are randomly initialized.
  Agent adds noise to policy output for exploration.
  Each action results in a reward and a new state, and these experiences are stored in replay buffer.
  During training, mini-batches of experiences are sampled from this buffer.
  Critic updates minimize MSE between predicted and target Q-values.
  Actor updated using policy gradients to increase expected return. (calculating the gradient of the Q-value with respect to the action).
  Target networks updated slowly for stability using a smoothing factor.

## Slide 17
Compare performances with alternative methods by testing the model on the test datset
1
2
6
3
4
5
Validate the model by a simulation campaign
Train the agent with random starting positions and maps from training dataset until convergence to optimal policy
Import obstacles and density maps along with noise model
Configure algorithm’s hyperparametrs
Set up actor and critic neural networks
Implementation

## Slide 18
Hyperparametr Tuning

## Slide 19
State Representation
The state representation is a 24-dimensional vector, with the features corresponding to the input layer of the actor/critic neural networks.
  Drone’s Position: The cartesian coordinates of the drone in XY plane.
  Target’s Position: The cartesian coordinates of the target in XY plane.
  Distance to Target: The Euclidean distance from the drone to the target.
  Target Orientation: The orientation of the target with respect to the drone, represented as an angle in the XY plane.
  Local Population Density: The population density at the current drone location.
  Mean Population Density: The mean population density across two sub grids of sizes 15x15 and 51x51, with the drone at the centre of each.
  Orientation of Maximum Population Density: The orientation of the point of maximum population density in the sub grid with respect to the drone.
  Noise Level: The overall SPL value on the ground.
  Obstacle Distances: The distances from the drone to the three closest and three furthest obstacles.
  Obstacle Orientations: The orientations of these six obstacles with respect to the drone.

## Slide 20
The reward function plays a pivotal role in achieving the desired behavior from the model. It’s crucial to set the components of the reward function to guide it towards achieving optimal path and policy.
  Idle Penalty:
  Distance Penalty:
  Population Density Penalty:
Reward function

## Slide 21
  Noise Penalty:
  Cumulative Noise Penalty:
  Smoothness Penalty:
  Reward Function:
Reward function

## Slide 22
Training Phase

## Slide 23
Results

## Slide 30
Model Validation

## Slide 32
Application
  The use of UAVs for delivery purposes is rapidly gaining traction in commercial sectors.
  However, current commercial drones typically lack advanced automatic control systems and are not optimized to achieve specific operational objectives, such as minimizing noise pollution.
  Machine Learning models’ flexibility is crucial since not all delivery packages have the same priority or urgency, necessitating adaptable control strategies.
  To cater to different delivery scenarios, two versions of the RL model were developed.
  High-Priority Delivery: In scenarios where timely delivery is critical, such as delivering medical supplies to a hospital, the model emphasizes on reducing delivery time over noise minimization and optimizes the flight path primarily for speed and efficiency, accepting higher noise levels as a trade-off.
  Low-Priority Delivery: For deliveries that do not require urgency, such as regular postal services, the model focuses on minimizing noise impact while still ensuring reasonable delivery times. This mode focuses on optimizing flight paths to reduce noise pollution, even if it means longer delivery times and is beneficial in residential or sensitive areas.

## Slide 37
Conclusion
  Demonstrated the effectiveness of Reinforcement Learning (RL) in noise-aware UAV path planning.
  RL agent balanced path length and noise control, outperforming traditional methods.
  RL agent reduced noise per unit length and achieved lower minimum noise levels on longer trajectories, highlighting effective noise-sensitive navigation.
  Managed noise through dynamic adaptation of velocity based on environmental noise sensitivity.
  Prioritized noise-sensitive navigation while maintaining overall travel efficiency.
  Showcased adaptability, generalization, and effectiveness in noise-sensitive environments.
  Offered promising solutions for sophisticated UAS navigation.

## Slide 38
Integrate machine learning models with lidar data and Convolutional Neural Networks (CNNs) for dynamic noise prediction adjustments.
Future Development
RECOMMENDATION 3
Integrate Recurrent Neural Networks (RNNs) to capture temporal dependencies in UAV navigation tasks, leading to more adaptive and responsive strategies.
RECOMMENDATION 4
Improve accuracy and realism of noise modeling by incorporating actual noise signals emitted by UAVs.
RECOMMENDATION 1
Utilize high-resolution maps including vegetation density, building layouts, and terrain variations for refined noise predictions.
RECOMMENDATION 2

## Slide 39
Thank You
Shahin Sarhan | Politecnico di Torino