## Slide 1
Application of Value Stream Mapping in High-Mix Low-Volume (HMLV) Manufacturing
Supervisor: Prof. Giulia Bruno
Oct 2025
Master Degree in Engineering and Management
ANGEL ZACARIAS BENITEZ MARTINEZ

## Slide 2: Thesis Outline
Introduction
Motivation
State of the art
Methodology framework
Case study: analysis and results
Conclusions
Notes: Begin with a brief intro and motivation
Summarize the state of the art analysis and foundations
Explain the methodology framework
Present the case study and its main findings
Conclude with key takeaways and future research directions

## Slide 3: Introduction
Angel Benitez – Application of Value Stream Mapping in High-Mix Low-Volume (HMLV) Manufacturing
3
Digital/Adaptive Lean
Lean expands into HMLV&ETO
Lean Production
Toyota Production System
Mass Production
Craft Production
1800s
1913
1950
1990
2000s
2020s
Notes: Animations
The goal of this work is to build on the evolution of production systems, from craft production back in the days, to the 50’s where Toyota production system was finally introduced. This served as the foundation for the development of Lean manufacturing, a philosophy that changed our way of seeing efficiency, focusing on waste identification and the concept of continuous improvement.
However, the industry keeps evolving, moving towards more customized products, leaving lean tools shorthanded facing new challenges in this new environment.
So this work investigates how lean tools can be tailored for a specific scenario.

## Slide 4: Motivation
4
Angel Benitez – Application of Value Stream Mapping in High-Mix Low-Volume (HMLV) Manufacturing
Documents analysis from Gan et al. (2023)
Notes: Explain a bit better the graph to highlight the importance.
The scope of this work focuses on HMLV settings, as they are getting more relevant lately due to the market trend
The number of investigations in academia is naturally growing along
SMEs have a huge importance in the economy and have an important productivity gap
They could use lean tools to improve their productivity
All this gives us ground to deepen our exploration on how important tools can be of help

## Slide 5: State of the Art
5
Analysis breakdown
Reviews and Frameworks
Process improvement in complex manufacturing environments
Value Stream Mapping: Evolution and applications
Angel Benitez – Application of Value Stream Mapping in High-Mix Low-Volume (HMLV) Manufacturing
Notes: Literature shows an increasing interest in applying VSM and lean tools to non-traditional settings, which could be infered is due to the productivity gaps they face.
The analysis was basically organized in 3 group of papers:
Review and frameworks: These papers take a broad, synthesizing view, mapping what’s known about Lean (LM), High-Mix/Low-Volume (HMLV), Engineer-to-Order (ETO), and the role of VSM, often proposing organizing frameworks or research agendas
Process improv. In compelx manuf. Env.: This group reports hands-on interventions (kaizen, pull, line redesign) in HMLV/MTO/ETO-like settings, quantifying lead-time, WIP and efficiency gains when lean tools are tailored to complexity.
VSM evolution and applications: These papers center on the application and evolution of Value Stream Mapping as a tool for identifying inefficiencies and driving process improvements, exploring integration with other tools, digitalization, etc.

## Slide 6: Methodology framework
6
Angel Benitez – Aplication of Value Stream Mapping in High-Mix Low-Volume (HMLV) Manufacturing
Notes: This work uses already existing frameworks with small changes tailored to the current circumstances.
The first part consists in selecting a representative family of products which would be chosen based on defined and well explained criteria.
The second part corresponds to the elaboration of the current state VSM
The third step implies the analysis of waste identified in the current state VSM
The fourth step consists in the elaboration of the future state VSM, based on the recommendations given in the analysis phase.
Finally, the implementation plan and the corresponding execution.

## Slide 7: Case study: analysis and results
The Company
7
Main product types
TRAP
CIL
TAZZA
GOLA
Angel Benitez – Application of Value Stream Mapping in High-Mix Low-Volume (HMLV) Manufacturing
HMLV - ETO
Notes: The case study took place in a company based here in Turin, a small-to-medium size enterprise producing diamond tools for the glass and ceramic industry.
The company manufactures a wide variety of products which are characterized according to the machine and the kind of work it has to perform to have a certain output.
The heterogeneity of the products makes it an ideal example of HMLV settings.

## Slide 8: Case study: analysis and results
8
Production proportion
Angel Benitez – Application of Value Stream Mapping in High-Mix Low-Volume (HMLV) Manufacturing
Notes: In the present slide we can see that roughly 4/5 of the products belong to repetitive models, although they may have differences in diameter. The rest corresponds to ETO products.
Within the repetitive models we can also see that there is a gap between the products ordered and delivered, having the biggest gap in the TRAP model.

## Slide 9: Case study: analysis and results
9
Angel Benitez – Application of Value Stream Mapping in High-Mix Low-Volume (HMLV) Manufacturing
Product | Steps | Affinity
TRAP100-150 | 16 | -
TRAP200 | 14 | 88%
CIL100-150 | 12 | 75%
CIL200 | 11 | 69%
TAZZA | 10 | 63%
G60-80 | 10 | 63%
G100-175 | 13 | 81%
G200 | 12 | 75%
Product family grouping
Notes: If we group the main repetitive models with their different diameters in families, we can compare the affinity they have in terms of process steps.
Now using the previous slide and this one, we can conclude infer that improving a single model, the trap 100-150, we would be improving customer satisfaction securing that products requested are delivered on time, and also we would be improving production time for the rest of the products.

## Slide 10: Case study: analysis and results
10
Angel Benitez – Application of Value Stream Mapping in High-Mix Low-Volume (HMLV) Manufacturing
Current State Map
Unit: min
Notes: Add animation
Add time unit
Take out the yellow bubbles
After a careful on-site observation, operators interview and manual data collection, I was able to build this VSM, that helped me realize some important points:
I found long lead times, mostly due to waiting times and overprocessing. Also, I could see some excess in transportation and inventory.
These inefficiencies showed the opportunity for improvement in the production process.

## Slide 11: Case study: analysis and results
11
Angel Benitez – Application of Value Stream Mapping in High-Mix Low-Volume (HMLV) Manufacturing
Analysis
Notes: So the analysis had several tools involved. The first one was a spaghetti map, that showed a very disorganized movement of the product, which indeed was creating transportation waste.
Also, a fishbone diagram was elaborated to analyze the long delivery time, identifying main causes related to this problem.
Finally, a 5Whys form was used to search for the root cause of the problem identify in the fishbone diagram. This tool proposed a challenge for the engineering department, consisting in the simplification of the workflow given the amount of overprocessing and transportation of the process.

## Slide 12: Case study: analysis and results
12
Angel Benitez – Application of Value Stream Mapping in High-Mix Low-Volume (HMLV) Manufacturing
Current State Map
Unit: min
Notes: Add animation
Add time unit
After a careful on-site observation, operators interview and manual data collection, I was able to build this VSM, that helped me realize some important points:
I found long lead times, mostly due to waiting times and overprocessing. Also, I could see some excess in transportation and inventory.
These inefficiencies showed the opportunity for improvement in the production process.

## Slide 13: Case study: analysis and results
13
Angel Benitez – Application of Value Stream Mapping in High-Mix Low-Volume (HMLV) Manufacturing
Future State Map
Unit: min
Notes: Highlight the time change, the process change
Add time unit
The engineering department along with the operators were able to propose an enhancement to the process, thanks to which a future state map was elaborated and worked to implement.
It is also important to mention that the future state map contemplates modifications due to other ongoing projects that would impact positively in the outcomes that were being tried to get improved.

## Slide 14: Case study: analysis and results
14
Angel Benitez – Application of Value Stream Mapping in High-Mix Low-Volume (HMLV) Manufacturing
Results
Key metric | Before | After | Saving
CT (min) | 1874 | 1005 | 870
L (min) | 5930 | 2005 | 3925
WIP (batches) | 7 | 3 | 4
TAKT TIME (min) | 1045 | 450 | 595
Distance (m) | 170 | 125 | 45
Notes: Afte the implementation of the future state map, with the new layout and the modifications applied to the process, produced significant improvements in the process, getting much better numbers for all key indictors of the production process.
The indicators measured are…

## Slide 15: Conclusions
15
Angel Benitez – Application of Value Stream Mapping in High-Mix Low-Volume (HMLV) Manufacturing
VSM proved to be effective beyond mass production but needs adaptation to work effectively.
The case study proved that if well adapted, the tool can provide important gains in relevant KPIs for the companies.
Future works (for the company)

## Slide 16
Thank you!