## Slide 1
BIM-LCA Approach for Carbon Footprint Reduction of Building Envelope Insulation:
A Residential Case Study in Chieri, Turin

## Slide 2: Glowbal warming problem
Building section
Share of buildings in global energy and
process emissions in 2022

## Slide 3: The question is:
How can we reduce the amount of that in building sector?
Which include 85% of total amount of CO2 emissions which is a huge number
The answer is not one answer and there are different methodology and approach.

## Slide 4: Residential case in Chieri, To
In this study, as I started my internship in studio 74 and we have started a restoration, renovation project, I decided to study on this real project and take one step.
Introducing building, 2 floors,
The problems: mold and humidity
Solusion: insulation
Limitation: Rules of Chieri

## Slide 6: Methodology

## Slide 7: Modeling in Revit
Starting from point cloud for 3D modelling drawing
Drawing levels and external walls
Decision: working on insulation layers of external walls
External walls drawing method
Sceario 1
Scenario 2
Insulation layers methodogy
Sceario 1
Scenario 2
International Energy Agency (IEA). (2023). Tracking Clean Energy Progress (adapted by GlobalABC / UNEP). Retrieved from https://www.iea.org/reports/tracking-clean-energy-progress

## Slide 8
1. Establishing Levels: Levels corresponding to the point cloud data were established to maintain consistency across the model.
2. Modeling Walls
First approach:
Using the "Model In-Place" Option: To achieve high accuracy, particularly in representing the irregular walls characteristic of historical buildings, the "Model In-Place" tool was utilized.
Second approach:
Irregular sections were merged with column components, which automatically adopted the material properties of the outermost wall layer. This allowed for the representation of both irregular geometries and wall stratigraphy simultaneously.
Second approach
First approach
Modeling Walls

## Slide 9: 2. Modeling Insulation Options
Approach 1: Drawing External Walls with Separate Insulation Layer
Methodology
Sustainability Considerations
Challenges
Approach 2: Drawing Walls with Integrated Layers
Methodology
Sustainability Considerations
Challenges
integrating insulation within the wall assembly and modeling it as a separate wall component. The second method—drawing insulation as its own layer—proved more suitable for LCA purposes.

## Slide 10: Example of graphic and alphanumerical contents of the LOD

## Slide 11: Workflow for Preparing Revit Model for LCA Analysis
1.Create a New Workset
2.Select External Walls
3.Assign to Workset
4.Repeat for Doors, Windows, and Roofs
5.Verification of Accuracy

## Slide 12: Workflow for Preparing Revit Model for LCA Analysis
Step 1 — Duplicate the Base View
Step 2 — Control Workset Visibility
Step 3 — Creation of a View Template

## Slide 13
Life Cycle Assessment

## Slide 14: Life Cycle Assessment
How to select the tool based on different tools?
Tally:
One Click LCA

## Slide 15: Tally and One Click LCA
Tally results
One click LCA results:

## Slide 16: Dynamo
Data Export and Dynamo Integration
Using the information of LCA calculation in Revit automatically by Dynamo.
The process: excel file -> Dynamo -> Revit -> Color-coding – Visualization

## Slide 17: Dynamo
Step 1 – Extracting Valid Geometry Walls
Step 2 – Dividing the List based on the Insulation Thickness
Step 4 – Reading and Analyzing the Excel Data

## Slide 18: Color-Coding
Filters Categories in Revit
Screenshot of the Results of Dynamo atomization in Revit
Color Filters Visibility in Revit

## Slide 19: Color-Coding & Visulization

## Slide 20: Conclusion
Chart: GWP Comparison (kg CO₂e)
| 40 mm | 100 mm | 140 mm
EPS - GWP | 3.66 | 7.74 | 10.56
MW - GWP | 5.25 | 11.11 | 15.15
Comparison both EPS and Mineral wool results by Tally in Excel
comparison of Multipor Xella insulation layer at three thicknesses from both plugins