## Slide 1: Investigation of Transient Resonance Response in Bladed Disks
Supervisors:
Prof. Christian Maria Firrone
Prof. Daniele Botto
Ing. Antonio Giuseppe D’Ettole
Ing. Gianmaria Sartor
Master’s Degree in Mechanical Engineering
Credits: front image – GE Aviation
Candidate:
Lorito Ethan Raoul (332003)
MSc. Thesis

## Slide 2: SUMMARY
Introduction
Aeromechanics in Turbomachinery
SDOF sensitivity analysis of transient response
Experimental Validation
Conclusions

## Slide 3
INTRODUCTION

## Slide 4: INTRODUCTION
Motivation
Unconventional dynamic responses of bladed disks
Possible explanation as transient effects
Prediction capability before test campaign
Objective
Investigation of transient effects in dynamic response and justification of observed response
Confirm the capability of commercial FEM tools to predict them in the design phase
Observed response (1)
SDOF
Spin Test
3D FEA
(1) Luigi Carassale, Michela Marrè-Brunenghi, Stefano Patrone, Wavelet-based identification of rotor blades in passage-through-resonance tests, Mechanical Systems and Signal Processing, Volume 98, 2018, Pages 124-138, ISSN 0888-3270.

## Slide 5
AEROMECHANICS IN TURBOMACHINERY

## Slide 6: AEROMECHANICS IN TURBOMACHINERY – Forced Response
Aeromechanics studies the interaction of elastic bodies with fluid flows.
The two principal problems are:
Forced Response: vibration with defined amplitude
Flutter: Increasing vibration or limit-cycle oscillation
In case of Forced Response:
Forces acting on the rotating blade from
aero unsteadiness
FFT of pressure signal
Travelling Wave excitation
Engine Order

## Slide 7: AEROMECHANICS IN TURBOMACHINERY – Nodal Diameters
Bladed Disk with N Sectors
Fundamental Sector
: Inter-Blade Phase Angle (IBPA)
The motion of one sector is out of phase by an angle φ with respect to the adjacent sector.
Harmonic Index (h): order of the harmonic function. Defines the phase delay.
Nodal Diameters (ND): h diametric lines characterized by zero displacement
ND 0
ND 1
ND 3

## Slide 8
A certain EOs excites a ND if:
Exciting frequency is equal to the natural frequency of the mode and
Travelling Wave couples with the mode shape
AEROMECHANICS IN TURBOMACHINERY – Critical Crossings
Campbell Diagram
Not all crossings are critical

## Slide 9
AEROMECHANICS IN TURBOMACHINERY – Non-Synchronous Vibrations
Non-Synchronous Vibration
Synchronous Vibration
Possible explanations for NSVs:
Flutter
Separated Flow Vibration
Rotating Stall
TRANSIENT RESONANCE CROSSING
The fast sweep through resonance doesn’t allow the Homogenous response to decay
Horizontal trace in Campbell diagram.

## Slide 10
SDOF SENSITIVITY ANALYSIS

## Slide 11: SENSITIVITY ANALYSIS – Effect of the Reduced Sweep Velocity
The transient response is governed by the Reduced Sweep Velocity (RSV or K):
With:
Maximum amplitude shift in the direction of sweep
Amplitude decreases with respect to steady state
response
Resonance peak’s width increases
Beating phenomenon for (2)
Transient effects can explain observed NSVs
(2) Hackenberg, H., Hartung, A. (March 15, 2016). "An Approach for Estimating the Effect of
Transient Sweep Through a Resonance." ASME. J. Eng. Gas Turbines Power. August 2016;
138(8): 082502.

## Slide 12
EXPERIMENTAL VALIDATION

## Slide 13: EXPERIMENTAL VALIDATION – Test Article
Test Campaign conducted on a dummy blisk to evaluate the Transient Resonance Response when crossing resonances at high sweep rates
N° of Blades | 12
Disk Material | Aluminum
Magnets Material | Neodymium
Magnets for non-contact excitation during rotation: one per blade tip
Test Article: Dummy Blisk

## Slide 14: EXPERIMENTAL VALIDATION – Spinning Test Rig
Static Ring 1
Static Ring 2
Bladed Disk
Rig housed into a sealed pit capable of maintaining a vacuum environment to remove the fluid structure interaction
during the tests.
Dynamic response measured via Strain Gauges (SGs) in half-bridge configuration: 2 SGs on opposite side of each blade.
Dummy blisk excited by static permanent magnets on a static ring
SG Configuration | Half-Bridge
Static Magnets N° | 1
Max rotation speed [RPM] | 4000
Manner telemetry system for transmission of SGs data during spin test
Strain Gauge position

## Slide 15: EXPERIMENTAL VALIDATION – Spinning Test Rig
Static Ring 1
Static Ring 2
Excitation System
BTT Sensors
Bladed Disk
Strain Gauges

## Slide 16: EXPERIMENTAL VALIDATION – Test Campaign
The Test Campaign included six different tests characterized by sweeps with different speeds and directions.
Test Name | Sweep Rate [RPM/s] | SG Sampling Frequency [Hz] | Sweep Direction
1 | 1 | 1000 | Up
2 | 16 | 1000 | Up
3 | 16 | 14000 | Up
4 | 16 | 14000 | Down
5 | 64 | 14000 | Up
6 | 64 | 14000 | Down
Test 3 was chosen for the experimental validation of numerical results:
Good separation between responses of different modes
Highest sampling frequency
Shorter duration of the runs compared to Test 1
ND 3
ND 4
ND 5
Test 3 – SG 1 Time History
In the speed range of Test 3, three Nodal Diameters showed a
clear response:
ND 3 - ND 4 - ND 5 excited by EO 7 – EO 8 – EO 9

## Slide 17
FEM TRANSIENT ANALYSIS

## Slide 18: FEM TRANSIENT ANALYSIS – Finite Element Model construction
The tests have been replicated on Ansys Mechanical APDL 2022 R2 to assess the capability of the FEM to predict transient
effects in a 3D Dynamic Analysis.
Test Article Finite Element Model
Single Sector
Full 360 Model
Aluminum alloy | 
Young’s modulus [Gpa] | 74
Poisson’s ratio | 0.33
Density [kg/cm3] | 2780
Neodymium | 
Young’s modulus [Gpa] | 160
Poisson’s ratio | 0.24
Density [kg/cm3] | 7300
Constraints Radius [m] | 0.041
3D Solid Element | Solid95
Aluminum alloy | 
Young’s modulus [Gpa] | 74
Poisson’s ratio | 0.33
Density [kg/cm3] | 2780
Neodymium | 
Young’s modulus [Gpa] | 160
Poisson’s ratio | 0.24
Density [kg/cm3] | 7300
Constraints Radius [m] | 
3D Solid Element | Solid95

## Slide 19: FEM TRANSIENT ANALYSIS – Model Tuning
The model has been tuned with respect to the FRF obtained from a Non-Rotating Hammer Test in air.
 | ND 3 | ND 4 | ND 5
Natural Frequency Hammer Test [Hz] | 144.1 | 150.2 | 154.1
Natural Frequency Numerical [Hz] | 144.6 | 149.3 | 152.6
Error [%] | 0.30 | 0.63 | 0.96
The same test has been used for the identification of the Damping ratio, since:
Hammer test in vacuum conditions is precluded
No steady state test data available – beatings present even at
lowest sweep rate (Test 1)
 | ND 3 | ND 4 | ND 5
Damping Ratio | 5.32E-04 | 5.03E-4 | 1.75E-04
ND 3
ND 4
ND 5
ND 0
ND 1
ND 2
ND 6
Frequency [Hz]
FRF Magnitude (db [m/Ns])
Non-Rotating Hammer Test damping used as reference

## Slide 20: FEM TRANSIENT ANALYSIS – Centrifugal Stiffening
The effect of centrifugal stiffening is considered in the preparation for numerical analyses
EO 7
EO 9
EO 8
Pre-stressed Modal
 | ND 3 | ND 4 | ND 5
Engine Order | 9 | 8 | 7
Rotor Speed [RPM] | 1004.28 | 1172.85 | 1372.60
Natural Frequency Test [Hz] | 146.5 | 153.0 | 157.5
Natural Frequency Numerical [Hz] | 146.1 | 151.4 | 155.4
Error [%] | 0.27 | 1.05 | 1.34
Good tuning between experimental and numerical frequencies

## Slide 21: FEM TRANSIENT ANALYSIS – Travelling Wave excitation
Travelling Wave (EO 5)
Applied load
FE Model ready to run transient analysis

## Slide 22: EXPERIMENTAL VALIDATION – Test Results
EO 7 – ND 5
Good correlation between FEM and SG signal
Sweep Rate: 16 RPM/s
 | SG 1 | FEM | Error [%]
 | 60.1 | 58.4 | 2.80
 | 60.8 | 59.0 | 2.96
 | 9.28E-4 | 9.30E-4 | 0.21
 | 7.10E-4 | 7.14E-4 | 0.56
 | 0.765 | 0.768 | 0.35
 | SG 1 | FEM | Error [%]
 | 60.1 | 58.4 | 2.80
 | 60.8 | 59.0 | 2.96
 | 9.28E-4 | 9.30E-4 | 0.21
 | 7.10E-4 | 7.14E-4 | 0.56
 | 0.765 | 0.768 | 0.35

## Slide 23: EXPERIMENTAL VALIDATION – Test Results
EO 8 – ND 4
 | SG 1 | FEM | Error [%]
 | 46.7 | 46.0 | 1.50
 | 47.3 | 46.6 | 1.48
 | 8.97E-4 | 9.05E-4 | 0.89
 | 6.47E-4 | 6.05E-4 | 6.49
 | 0.721 | 0.669 | 7.21
 | SG 1 | FEM | Error [%]
 | 46.7 | 46.0 | 1.50
 | 47.3 | 46.6 | 1.48
 | 8.97E-4 | 9.05E-4 | 0.89
 | 6.47E-4 | 6.05E-4 | 6.49
 | 0.721 | 0.669 | 7.21
Sweep Rate: 16 RPM/s
Good correlation, small variations due to mistuning

## Slide 24: EXPERIMENTAL VALIDATION – Test Results
EO 9 – ND 3
 | SG 1 | FEM | Error [%]
 | 35.3 | 35.9 | 1.69
 | 35.9 | 36.4 | 1.39
 | 6.85E-4 | 6.85E-4 | 0.01
 | 3.32E-4 | 4.67E-4 | 40.7
 | 0.485 | 0.682 | 40.6
 | SG 1 | FEM | Error [%]
 | 35.3 | 35.9 | 1.69
 | 35.9 | 36.4 | 1.39
 | 6.85E-4 | 6.85E-4 | 0.01
 | 3.32E-4 | 4.67E-4 | 40.7
 | 0.485 | 0.682 | 40.6
Sweep Rate: 16 RPM/s
Worse correlation but conservative

## Slide 25: Future works
Transient effects are a cause for Non-Synchronous Vibrations in bladed disks, particularly in presence of low
damping and high sweep rates
They can affect the correct identification of modal parameters
For the test case, commercial FEM tools can accurately predict the dynamic response in transient conditions
Conclusions
Extend the investigation to a mistuned FE model
Verify that another measurement technique, like BTT, is able to capture transient effects