## Slide 1: Politecnico di Torino Department of Environment, Land and Infrastructure Engineering Master of Science in Georesources and Geoenergy Engineering Design of a Plant for Sulfur Oxides Production and Recovery Candidate: Mehran Moazeni Targhi Supervisors: Prof. Fabio Alessandro Deorsola Prof. Samir Bensaid July 2026
Notes: Good morning/afternoon everyone. My name is Mehran Moazeni Targhi, and today I will present my Master's thesis entitled "Design of a Plant for Sulfur oxides Production and recovery" This work was carried out under the supervision of Professor Deorsola and Professor Bensaid at Politecnico di Torino. The project focuses on developing a rigorous process simulation of an industrial sulfur dioxide production plant, validating the model against industrial operating data, and investigating opportunities for improving energy recovery using process integration techniques.

## Slide 2: Introduction
Sulfur dioxide plant design and Heat recovery scenarios
Background research and studies
Heat and material balance
Heat transfer coefficient and area calculation
Simulation with Aspen Plus
Sensitivity analysis scenarios
Energy integration and Pinch technology

## Slide 3: Background: 33 processes, 3 Gas Cleaning Technologies, 10 Purification technologies
No. | Sulfur source/feed | Technology/ furnace type | Main reaction(s) | Typical operating conditions
Liquid | Elemental sulfur (liquid sulfur) | Liquid sulfur combustion furnace, Pressure-nozzle burner furnace, Two-component burner furnace, Rotary burner sulfur furnace (Lurgi/LURO burner), Two-stage sulfur combustion | S+O2​→SO2​ | Air :1.3–1.5 bar at 60–100 °C. Liquid sulfur: 140–150 °C.In industrial operation, SO₂ concentration ~18 vol%.
Solid | Pyrite, Gold-bearing ores, Arsenical pyrite, Sulfides of Copper, Nickel, Zinc, Lead ores, Calcium sulfate (gypsum), Iron (II) sulfate and etc. | Roasting of Pyrites occurs in a flotation mode, Dorr-Oliver fluo solids reactor (wet feeding principle), Circulating fluid-bed (CFB) roasting (Lurgi technology) , Cyclone furnace roasting, Flash smelting furnace, Electric furnace smelting | Cu2S 2ZnS+3O2​→2ZnO+2SO2 2PbS+2.5O2​→Pb+PbO+2SO2​ | The optimum operating range is usually between 850 and 940 °C, 13–14 vol% is more typical due to excess air, fluidized-bed design operates on a wet feeding principle,
Gas | Waste sulfuric acid processing, Hydrogen sulfide (H₂S) Flue gases (low SO₂ content), | Thermal decomposition furnace, Grillo rotary kiln process, Catalytic incineration, the Claus process converts H₂S to elemental sulfur | H2​SO4​→SO2​+H2​O+O2​ | The decomposition of sulfuric acid at 1000 °C. catalyst at 200 °C . Regeneration at 600–650 °C.
No. | Sulfur source/feed | Technology/ furnace type | Main reaction(s) | Typical operating conditions
Liquid | Elemental sulfur (liquid sulfur) | Liquid sulfur combustion furnace, Pressure-nozzle burner furnace, Two-component burner furnace, Rotary burner sulfur furnace (Lurgi/LURO burner), Two-stage sulfur combustion | S+O2​→SO2​ | Air :1.3–1.5 bar at 60–100 °C. Liquid sulfur: 140–150 °C.In industrial operation, SO₂ concentration ~18 vol%.
Solid | Pyrite, Gold-bearing ores, Arsenical pyrite, Sulfides of Copper, Nickel, Zinc, Lead ores, Calcium sulfate (gypsum), Iron (II) sulfate and etc. | Roasting of Pyrites occurs in a flotation mode, Dorr-Oliver fluo solids reactor (wet feeding principle), Circulating fluid-bed (CFB) roasting (Lurgi technology) , Cyclone furnace roasting, Flash smelting furnace, Electric furnace smelting |  | The optimum operating range is usually between 850 and 940 °C, 13–14 vol% is more typical due to excess air, fluidized-bed design operates on a wet feeding principle,
Gas | Waste sulfuric acid processing, Hydrogen sulfide (H₂S) Flue gases (low SO₂ content), | Thermal decomposition furnace, Grillo rotary kiln process, Catalytic incineration, the Claus process converts H₂S to elemental sulfur |  | The decomposition of sulfuric acid at 1000 °C. catalyst at 200 °C . Regeneration at 600–650 °C.
Notes: Before developing the simulation, I conducted a comprehensive literature review covering 33 sulfur dioxide production technologies, 3 gas cleaning technologies, and 10 sulfur dioxide recovery and purification technologies. The production technologies were categorized according to the sulfur feedstock, including gaseous feeds such as hydrogen sulfide and flue gases, liquid feeds such as elemental sulfur and waste sulfuric acid, and solid feeds such as pyrite, copper, zinc, nickel, and lead sulfide ores. Different industrial technologies were reviewed, including sulfur combustion furnaces, fluidized-bed roasters, flash smelting furnaces, cyclone furnaces, rotary kilns, and Claus-based processes. The comparison showed that operating temperatures range from approximately 200°C to 1800°C, depending on the process, while sulfur dioxide concentration varies from 1–2 vol% in conventional metallurgical processes to 80–85 vol% in oxygen-enriched smelting technologies. However, modern sulfur-burning plants typically produce around 18 vol% SO₂, which provides a suitable concentration for efficient heat recovery and sulfuric acid production. The review also showed that modern plants integrate waste heat recovery with gas cleaning and recovery technologies such as partial condensation, water absorption, and physical absorption to improve both energy efficiency and product quality.

## Slide 4
Notes: This thesis focuses on the liquid sulfur combustion process, which is the most common industrial technology for sulfur dioxide production. Liquid sulfur is fed to the furnace at approximately 135°C and 24.5 bar, while combustion air is preheated to 105°C before entering the furnace. ( later one of the scenarios can be to use the outlet heat for preheating the air) Inside the sulfur furnace, the main combustion reaction occurs: S+O2→SO2 ​ This highly exothermic reaction produces a flame temperature of approximately 1700°C. As the hot gas is cooled through the waste heat recovery system, if there would be enough excess oxygen, a small fraction of sulfur dioxide can be further oxidized to sulfur trioxide, particularly when the gas temperature decreases to around 700–750°C: 2SO2+O2⇌2SO3 ​ The recovered heat is simultaneously used to produce high-pressure superheated steam at approximately 450°C and 37.46 bar, which can be utilized for electricity generation or other plant utilities. The sulfur trioxide formed can then react with water vapor in the inlet air according to: 2SO2+O2⇌2SO3 ​ The recovered heat is simultaneously used to produce high-pressure superheated steam at approximately 450°C and 37.46 bar, which can be utilized for electricity generation or other plant utilities. The sulfur trioxide formed can then react with water vapor in the inlet air according to: SO3+H2O→H2SO4 ​ If the gas temperature falls below the sulfuric acid dew point, which is approximately 195°C under the operating conditions of this plant, sulfuric acid condenses on equipment surfaces and causes severe corrosion. Therefore, the outlet SO₂-rich gas is always maintained above the acid dew point before entering the sulfuric acid plant.

## Slide 5
Notes: This figure shows the detailed configuration of the sulfur furnace and its integrated heat recovery system. The industrial unit consists of two main sections: the sulfur combustion furnace, where sulfur is burned to produce sulfur dioxide, and the waste heat recovery system, which includes six consecutive heat recovery stages. Because of the large size, complex geometry, and customized industrial design of the furnace, it could not be represented by a single Aspen Plus block. Therefore, to accurately reproduce the temperature profile and the heat recovery, I divided the system into six individual heat exchangers and three reactor blocks.
The first three sections include the furnace (Evaporator 1), Evaporator 2, and Superheater 2. The combustion occurs in Evap1 and secondary oxidation reactions continue while the gas temperature decreases from approximately 1700°C to 790°C or less. The remaining units—Superheater 1, Evaporator 3, and Economizer—mainly recover the remaining sensible heat, cooling the gas sequentially from 734°C, 524°C, 469°C, to the final outlet temperature of 266°C. This outlet temperature is higher than the acid dew point which is around 200 C which approves the feasibility of extra heat recovery. During this heat recovery process, saturated steam is generated in the evaporators and then superheated in the two superheater stages to produce high-pressure superheated steam at approximately 450°C, which is supplied to the plant utilities or electricity generation system.

## Slide 6: Aspen Plus Model, Heat Recovery and Process Challenges
Notes: This slide presents the Aspen Plus process flow diagram developed for the industrial sulfur dioxide production plant. The plant contains several interconnected recycle loops involving steam, water, and combustion gas, making the simulation and numerical convergence particularly challenging. The heat recovery section was modeled using a separator–reboiler system together with pumps, valves, splitters, mixers, and heat exchangers. Make-up water enters the system and is mixed with part of the liquid leaving the separator before passing through the economizer and returning to the separator. The remaining liquid stream circulates through Evaporator 1, Evaporator 2, and Evaporator 3, before returning to the separator. The vapor leaving the separator is sent to Superheater 1, then through the internal heating coil inside the separator–reboiler, and finally to Superheater 2, producing high-pressure superheated steam at approximately 450°C.
One of the major challenges was modeling the separator internal heating coil and achieving stable convergence of the recycle loops. To overcome these challenges, several Design Specifications, convergence blocks, and iterative solution strategies were implemented. Unlike a conventional simulation, the outlet conditions of the heat exchangers were not predefined. Instead, the required heat-transfer surface area of each exchanger was calculated. For the studded tubes, fin efficiency was included in the calculations, and the overall heat-transfer coefficient was determined for each heat exchanger. The furnace and reaction zones were modeled using RGibbs reactors, allowing the chemical equilibrium to be calculated automatically.

## Slide 7: Aspen Plus Model, Heat Recovery and Process Challenges
Notes: This slide presents the Aspen Plus process flow diagram developed for the industrial sulfur dioxide production plant. The plant contains several interconnected recycle loops involving steam, water, and combustion gas, making the simulation and numerical convergence particularly challenging. The heat recovery section was modeled using a separator–reboiler system together with pumps, valves, splitters, mixers, and heat exchangers. Make-up water enters the system and is mixed with part of the liquid leaving the separator before passing through the economizer and returning to the separator. The remaining liquid stream circulates through Evaporator 1, Evaporator 2, and Evaporator 3, before returning to the separator. The vapor leaving the separator is sent to Superheater 1, then through the internal heating coil inside the separator–reboiler, and finally to Superheater 2, producing high-pressure superheated steam at approximately 450°C.
One of the major challenges was modeling the separator internal heating coil and achieving stable convergence of the recycle loops. To overcome these challenges, several Design Specifications, convergence blocks, and iterative solution strategies were implemented. Unlike a conventional simulation, the outlet conditions of the heat exchangers were not predefined. Instead, the required heat-transfer surface area of each exchanger was calculated. For the studded tubes, fin efficiency was included in the calculations, and the overall heat-transfer coefficient was determined for each heat exchanger. The furnace and reaction zones were modeled using RGibbs reactors, allowing the chemical equilibrium to be calculated automatically.

## Slide 8
Notes: The Aspen Plus results show good agreement with the available industrial data. The final outlet gas leaves the economizer at approximately 266°C, safely above the sulfuric acid dew point, with an SO₂ mole fraction of about 0.18. The heat recovery system also produces superheated steam at 450°C, suitable for turbine or utility use. The outlet composition is strongly dependent on the specific water content in the inlet air; if the air humidity changes, the formation of SO₃ and H₂SO₄ may also change, affecting the final gas composition, acid dew point, and corrosion risk.

## Slide 9
Notes: The T–Q curves confirm that all six heat exchangers operate without temperature crossing or pinch violation, demonstrating a thermodynamically feasible design. Heat-transfer areas and overall heat-transfer coefficients were calculated for each exchanger. Since EX-EVAP3 and EX-ECO employ finned tubes, fin-efficiency and effective heat-transfer area corrections were applied. The corrected overall heat-transfer coefficients were then implemented in Aspen Plus, resulting in good agreement between the simulation and the industrial operating data.

## Slide 10
Notes: Case 1 evaluates inlet air humidity from 0 to 336.3 kg/h H₂O. Increasing humidity reduces T_furnace because water vapor absorbs part of the combustion heat. At the same time, H₂SO₄ formation, acid dew point, and corrosion risk increase because more water is available to form sulfuric acid in the downstream cooling section. SO₂ outlet purity slightly decreases due to dilution. Case 2 evaluates inlet air temperature from 100 to 200°C. Higher inlet air temperature increases T_furnace because the air is already preheated, so less heat is consumed to warm the reactants. SO₂ outlet purity slightly increases, while H₂SO₄ formation, acid dew point, and corrosion risk decrease because higher temperature favors SO₂ over SO₃ formation, reducing sulfuric acid generation. Case 3 evaluates oxygen mass flow rate from 4389 to 6389 kg/h. Increasing oxygen reduces T_furnace because more gas flow must be heated, and SO₂ purity decreases mainly due to dilution. However, higher oxygen availability promotes further oxidation of SO₂ to SO₃, so H₂SO₄ formation, acid dew point, and corrosion risk increase.

## Slide 11
Notes: Case 4 – Inlet Air Flow Rate Case 4 investigates the effect of increasing the inlet air flow rate from 18,000 to 23,000 kg/h. A higher air flow increases oxygen availability, enhancing SO₂ oxidation to SO₃ and consequently increasing H₂SO₄ formation, acid dew point, and corrosion risk. At the same time, the larger gas flow reduces the furnace outlet temperature due to dilution, highlighting the need to carefully balance excess air to achieve efficient sulfur conversion while minimizing corrosion. Case 5 – Sulfur Feed Flow Rate Case 5 evaluates the effect of increasing the sulfur feed rate from 3,500 to 6,000 kg/h. Increasing sulfur feed raises the furnace heat release, steam production, heat recovery, separator pressure, and circulation flow, improving energy recovery. However, the higher operating temperature decreases SO₃ formation, H₂SO₄ concentration, acid dew point, and corrosion risk, while maintaining product quality. These results demonstrate that sulfur feed rate strongly influences both process performance and heat recovery and should be optimized for efficient plant operation.

## Slide 12
Notes: Composite Curve The composite curve combines all hot and cold process streams to determine the maximum theoretical heat recovery within the process. The large separation between the hot and cold curves at high temperatures indicates a significant amount of recoverable energy from sulfur combustion gases. As the curves approach each other at lower temperatures, the minimum temperature difference defines the pinch constraint, limiting additional internal heat recovery. Grand Composite Curve (GCC) The Grand Composite Curve represents the net heat surplus and deficit throughout the process after heat integration. It identifies the pinch location within the economizer section, indicating where external heating or cooling becomes unavoidable. Above the pinch, excess process heat is available for recovery, while below the pinch the remaining heat recovery is restricted by the minimum temperature approach and the sulfuric acid dew point limitation. Temperature vs. Cumulative Heat Load The Temperature versus Cumulative Heat Load plot represents the actual heat exchanger network rather than the theoretical heat recovery target. It illustrates how the sulfur combustion gases transfer heat sequentially to the process streams. The curve shows that the superheater reaches a pinch condition with essentially no temperature driving force, making it the most thermally constrained exchanger in the network. In contrast, the economizer still retains a finite driving force but its outlet temperature cannot be reduced further because it must remain above the sulfuric acid dew point to prevent sulfuric acid condensation and corrosion.
Pinch Design Rules No heat transfer across the pinch. No external heating below the pinch. No external cooling above the pinch. Maximize process-to-process heat recovery. Maintain the flue gas temperature above the sulfuric acid dew point to prevent corrosion. Key Findings High-temperature sulfur combustion gases provide substantial recoverable energy for steam generation. The Composite and Grand Composite Curves demonstrate a high potential for internal heat recovery with minimal utility demand. The Grand Composite Curve identifies the pinch in the economizer region, defining the thermodynamic limit for process integration. The actual T–Q diagram shows that the superheater operates with nearly zero temperature driving force, making it the practical bottleneck of the heat exchanger network. The economizer outlet temperature is ultimately constrained by the sulfuric acid dew point, ensuring safe operation while maximizing energy recovery.
This interpretation is consistent with the information shown on your slide: the GCC identifies the thermodynamic pinch near the economizer, while the actual T–Q curve shows that the superheater is the exchanger where the temperature driving force is effectively exhausted, making it the practical limiting unit in the implemented heat recovery network.

## Slide 13
Notes: The outlet gas leaving the sulfur combustion process has a temperature of approximately 266°C, while the sulfuric acid dew point is approximately 205°C. This temperature difference provides around 370 kW of recoverable thermal energy that can be utilized without cooling the gas below the acid dew point, thereby avoiding sulfuric acid condensation and corrosion. The proposed heat recovery system considers two practical utilization routes. The first option is to install an air preheater to recover waste heat and increase the combustion air temperature before entering the furnace, thereby improving the overall thermal efficiency and reducing fuel consumption. The second option is to implement a closed thermal oil loop, allowing the recovered heat to be transferred safely to other process streams or external heating applications where direct gas-to-process heat exchange is not feasible. The thermal oil analysis indicates that Therminol 66 is a suitable working fluid for the base operating condition due to its appropriate operating temperature range and thermal properties. For the base case, a thermal oil flow rate of approximately 3.1 kg/s is sufficient to recover the available heat. The sensitivity analysis further shows that the required oil circulation rate increases almost linearly with sulfur feed rate and recovered thermal duty. The comparison of commercial thermal oils demonstrates that several fluids are technically applicable; however, Therminol 66 provides the most practical balance between operating temperature capability, heat capacity, and industrial applicability, while Dowtherm A/VP-1 offers additional thermal stability for higher-temperature operating conditions.
Overall, the proposed heat recovery system demonstrates that low-grade waste heat can be effectively recovered from the outlet stream and reused within the process or exported to other plant units, resulting in improved energy efficiency, lower utility demand, and enhanced overall plant sustainability while maintaining operation above the sulfuric acid dew point.