## Slide 1: Conversion of an old biogas plant into a biomethane one
Thesis made by: Giuseppe Licata
Relator: Prof. Pierluigi Leone
Co-relator: Prof. Marco Cavana
In collaboration with Switch Engineering S.r.l. & Capwatt italia S.r.l.
Exploring the Transition from Biogas to Biomethane as a Sustainable Energy Solution through a real authorization project.
‘Dai diamanti non nasce niente…
Dal letame nascono i fior’
Cit. Fabrizio De Andrè
nasce il biometano’

## Slide 2: DM 2018 & DM 2022
The trajectory of biomethane sector development in Italy has been profoundly shaped by a series of successive ministerial decrees, each refining and adapting the policy landscape to evolving market conditions, technological advancements, and national energy imperatives. Among these, the Ministerial Decree of 2018 (DM 2018) and the Ministerial Decree of 2022 (DM 2022)
Timeline
DM 2022
Upgrade of last DM
DM 2012
First incentives for the production of biogas
-Electricity produced by CHP and sold to the grid at 0,28 €/kWh
DM 2018
First incentives for the production of biomethane
Gas injected into the grid
at 0,25 Scm/h
DM 2024
Last upgrade of DM 2022
Notes: The 2018 and 2022 decrees developed biomethane in Italy by introducing incentives, especially for the introduction of natural gas into the grid. The 2018 decree mainly promoted biomethane for transport, while the 2022 Ministerial Decree expanded the possibilities to include other uses (industrial, etc.), introducing capital support and an incentive tariff to promote new plants and the reconversion of existing biogas plants, also thanks to PNRR funding.

## Slide 3: Advantanges & Drawbacks of DM 2018
DM 2018 introduced several defining features that aimed to stimulate early market growth:
Targeted Focus on Agricultural Biogas
Fixed Feed-in Tariffs (FiTs) or Direct Premiums
Prioritization of Grid Injection
Incentives for Conversion
DM 2018 also faced certain limitations and challenges that necessitated subsequent policy adjustments:
Limited Feedstock Scope
Cost of incentives
Geographical concentration
Notes: Objective:
Promote the use of biomethane in transport, in line with European objectives on renewable fuels.
Incentives:
Incentive for the release of biofuels for consumption in transport, with the burden borne by the "Obligated Parties".
Promotion of the conversion of existing biogas plants.
Incentive for the production of other advanced biofuels other than biomethane.

## Slide 4: Improvements introduced by DM 2022
A crucial and transformative change introduced by DM 2022 was the substantial broadening of eligible feedstock. While DM 2018 primarily focused on agricultural biomass, the 2022 decree expanded the range to include a wider variety of organic waste streams, thereby unlocking significant untapped potential for biomethane production. This expansion specifically embraced:
FORSU;
Industrial by-products;
Sewage Sludge;
DM 2022 marked a strategic shift towards competitive auction mechanisms for allocating incentives, largely moving away from the fixed feed-in tariffs of the DM 2018, especially for larger capacities. This transition was driven by several key objectives:
Promoting Cost efficiency;
Market Orientation;
Scalability and predictability.
A core strategic objective of DM 2022 was its explicit and robust alignment with broader European directives and the National Recovery and Resilience Plan (PNRR).
Notes: Objective: To support the development of the production of biomethane to be fed into the natural gas network, drawing on PNRR funds. Types of incentivized plants: New agricultural or waste plants. Reconversion of existing biogas agricultural plants for the production of biomethane. Incentives: Capital support: Contribution of up to 40% of design and construction costs. Incentive tariff: Applied to the net production of biomethane, recognized for 15 years. It can be of two types: Premium rate: For biomethane that remains available to the applicant. All-inclusive tariff: For the withdrawal of biomethane by the GSE (for plants up to 250 \(m^{3}/h\)).

## Slide 5: How may a biomethane plant be designed and authorized?
1) Establish the feeding receipt according to the local available biomass, following the GSE’s rules in order to certify its sustainability
1
2) Make a constraint analysis on the plant’s site
2
3) Meet and keep in touch with the technical managers of Town, Province Region and Firemen for the permitting of the authorization documents
3
4) Create the Balance of mass and energy of the plant
4
5) Create the general layout following the BM&E and the other layouts needed for permitting;
5
6) Make all the documents requested by authorities and send them by PEC or upload in specific websites.
6

## Slide 6: The general process
Image Source: SNAM

## Slide 7: Balance of mass (1/2)

## Slide 8: Balance of mass (2/2)

## Slide 9: Resume of the plant’s balance of mass

## Slide 10: General layout

## Slide 11: The feeding recipt
[Scm/h] = G BIOMASS * ST * SV * MP * %CH4/Biogas
Ton/y = Biomass annual flow rate [ton/y]
ST = % of total Solids inside the biomas [%]
SV = % of Volatile matter inside the biomass [%]
MP = Methanigen Potential [Scm of CH4/ton of Volatile Matter]
% CH4/Biogas = 56 %
For guaranteeing the pumpability of the fluid
For guaranteeing the sustainability of receipt

## Slide 12: The anaerobic digestion section
> 40 days (by biologist’s esxperience)
Vu = Total useful volume of the vessels [m3]
QBIOMASS = Volume of biomass inside the vessels [m3/days]
The total amount of biogas is produced by the vessels
according to the following percentages:
Primary Digesters  70%
Secondary/Post Digesters  20%
Biogas Recovery tanks  10%

## Slide 13: Compliance with Seveso III directive
The Seveso III Directive (Directive 2012/18/EU) is a European regulation that requires industrial establishments handling dangerous substances to prevent and limit major accidents and their consequences for human health and the environment.
In the biogas field, the biogas mass must be lower than a certain level reccomended by the Firmen authorities in ordert to prevent explosions and consequently fire damages:
If the biogas mass stocked is over the limit, we evaluate of considering one of the vessels without dome in order to reduce

## Slide 14: From Digestion to Production

## Slide 15: The emergency torch
• Estimated biogas flow rate: 1,500 Nm3/h
• Nominal torch biogas flow rate: 1,900 Nm3/h
• Methane content in biogas: 40-80%
• Biogas pressure: 10/35 mbar
• Burning temperature: ≥ 1,000°C
• Smoke outlet height: 8 m
• Gas residence time in the room: >0.3 s
The purpose of the torch is to empty the anaerobic digestion tanks from the biogas produced, it will take approximately 4 hours, thus satisfying the 6 hours emptying time, as per the regional obligation.

## Slide 16: The Biogas Treatment unit
Before being used, biogas undergoes a series of treatments in order to eliminate hydrogen sulphide, water vapour and all impurities that can create problems during its subsequent uses. To eliminate some of the hydrogen sulfide, a knockdown tower is used where oxidoreductive reactions take place.
The biogas stream is sent to a tower where it is washed countercurrently by a chemical solution containing soda which is evenly distributed via a system of atomizing nozzles. The liquid obtained is rich in sulfur-containing compounds and is sent to a specific machine that allows the regeneration of the solution used in the desulfurization tower.

## Slide 17: The Upgrading
Variable | Project values | UoM
Temperature | 35 | °C
Pressure | 5 | mbar (g)
State of H20 | sature | 
Maximum wet biogas flow rate | 710 | Nm3/h
CH4 content | 50-60 | % V/V (=%mol)
N2 content | < 0,8 | % V/V (=%mol)
O2 content | < 0,6 | % V/V (=%mol)
CO2 content | 40-50 | % V/V (=%mol)
Variable | Project values | UoM
Temperature | 30 | °C
Pressure | 15 | bar (g)
Max BioCH4 flow rate | 750 | Sm3/h
CH4 content | >99 | % V/V (=%mol)
CO2 content | <1 | % V/V (=%mol)
N2 content | <0,8 | % V/V (=%mol)
O2 content | <0,6 | % V/V (=%mol)
H2S content | <6,6 | mg/Nm3

## Slide 18: The CHP
Technical Reference Data | Value
Operating cycle | 4-stroke
Unit displacement (12 cylinders) | 48.67 L
Fuel type | Biogas
Barometric pressure | 1 bar or 100 m a.s.l.
Relative humidity | 30%
Min/max ambient operating temperature | -15 / +35 °C
Total thermal power | 1,047 kWt
Nominal electrical power | 999 kWe
Fuel input power | 1,247 kW
Cogenerator dimensions (l×w×h) | 12.20 × 2.50 × 2.30 m
Exhaust gas emissions - NOx (at 5% O2) | < 450 mg/Nm³
Exhaust gas emissions - CO (at 5% O2) | < 500 mg/Nm³
Stack height | 10 m

## Slide 19: Balance of electrical energy

## Slide 20: Utilities
PLANT’S UNIT | POWER ABSORBED | YEARLY ELECTRICAL DEMAND | %
CHARGEMENT SYSTEM | 131 kWe | 1.140.365 kWh | 14%
OXYGENATION DURING ANAEROBIC DIGESTION | 17 kWe | 143.584 kWh | 2%
GENERAL SERVICES | 20 kWe | 170.000 kWh | 2%
DOPPIO SEPARATORE IN SERIE | 30 kWe | 508.282 kWh | 6%
UPGRADING | 439 kWe | 3.727.112 kWh | 45%
STRIPPAING | 80 kWe | 748.000 kWh | 9%
EVAPORATOR & OSMOSIS | 133 kWe | 1.144.240 kWh | 14%
GAS GRID COMPRESSOR | 87 kWe | 735.959 kWh | 8%
TOTAL | 937 kWe | 8.317.542 kWhe | 100%
Chart: YEARLY ELECTRICAL DEMAND %
| CHARGEMENT SYSTEM | OXYGENATION DURING ANAEROBIC DIGESTION | GENERAL SERVICES | DOUBLE SEPARATOR IN SERIE | UPGRADING | STRIPPING | EVAPORATOR & OSMOSIS | COMPRESSORE TO THE GAS GRID
YEARLY ELECTRICAL DEMAND % | 0.14 | 0.02 | 0.02 | 0.06 | 0.45 | 0.09 | 0.14 | 0.08

## Slide 21: Thermal flux P&ID

## Slide 22
Balance of thermal energy
Chart: 
| ANAEROBIC DIGESTION | POST-DIGESTION | EVAPORATOR | STRIPPING
YEARLY THERMAL DEMAND [kWht] | 4633342.6916 | 350313.4575 | 21615017.4043 | 867367.158
% | 0.16869 | 0.012754 | 0.78697 | 0.03158

## Slide 23
THANK YOU FOR YOUR ATTENTION