## Slide 1: Adversary Virtual Platform in Embedded System Environment for RED TEAM
Thesis Presentation
Master’s Degree in Computer Engineering
Supervisors:
Prof. Alessandro Savino
Prof. Stefano Di Carlo
Dr. Franco Oberti
Candidate:
Ismail Sanan

## Slide 2
Table of Contents
Introduction
Background on Embedded Systems Security
Virtual Platform: gem5
Spectre Attack SimulationReturn-to-Non-Secure (ret2ns) Attack
Experimental Results
Conclusions & Future Work

## Slide 3: Problem Statement
Embedded systems are critical infrastructure across industries but face significant security challenges:
Vulnerable to sophisticated attacks
Complex supply chain and legacy system
Widespread adoption in IoT, automative, healthcare, aerospace
Limited security testing capabilities

## Slide 4: Problem Statement
Key Challenge:
 Is it practical for red team operators to use a virtual platform to simulate hardware-based attacks?

## Slide 5: Objectives
This thesis aims to develop and evaluate Adversary Virtual Platforms (AVPs) for security testing of ARM based embedded systems.
Main Goals:
            Simulate realistic attack scenarios in controlled environments
                Demonstrate Spectre vulnerability exploitation
                Explore ret2ns attack in TrustZone-M systems
                Provide cost-effective alternative to physical hardware testing

## Slide 6: Background - Embedded Systems Security Why Security Matters
Memory attacks corrupt execution flow
Side-channels exploit CPU timing
behaviors
Privilege breaches bypass hardware isolation
Supply chain
understanding attacks at the microarchitectural level which gem5 enables through detailed simulation and analysis

## Slide 7: Virtual Platform - why gem5 Simulator
gem5: A Powerful Research Tool
        Open-source computer architecture simulator
        Supports multiple ISAs including ARM
        Full-system simulation mode
        System Emulation simulation mode
        Detailed microarchitectural modelling

## Slide 8: Virtual Platform - Simulation Setup
Full System Configuration:
Guest OS: Linux (vmlinux.arm64)
Bootloader: bbl-riscv_pkRoot
Filesystem: Linaro Minimal
AArch64CPU Model: Out-of-Order (O3)Cores: 3
Memory: 2GB DDR3

## Slide 9: Spectre Attack - Overview
What is Spectre?
A microarchitectural attack exploiting speculative execution to leak sensitive information.

## Slide 10: Spectre Attack - Overview
What is Spectre?
A microarchitectural attack exploiting speculative execution to leak sensitive information.
Why It Matters:
Affects multiple CPU vendors, Advanced Attack to bypass traditional security boundaries

## Slide 11: Spectre Attack - Simulation Process
Implementation Steps:
Compilation: Cross-compile Spectre exploit for ARM
2. gem5 Setup: Configure O3 CPU model with branch prediction
3. Execution: Run exploit in full-system mode
4. Data Collection: Extract data and cache timing
5. Visualization: Use Kotana for pipeline analysis

## Slide 12: Spectre Attack - Results
Successful Information Leakage Demonstrating
Key Findings:
✓ Spectre attack successfully simulated in gem5
✓ High score (999/999) indicates successful data extraction
✓ Pipeline visualization using Kotana for deeper analysis
✓ QEMU user-mode also validated attack feasibility

## Slide 13: ret2ns Attack - Overview
Return-to-Non-Secure Attack:
Exploits TrustZone-M's fast state-switching mechanism to redirect execution from secure to non-secure state with elevated privileges.
Attack Prerequisites:
Memory corruption in secure state
Vulnerable control-flow pointers (BXNS/BLXNS)
Lack of control-flow integrity checks
Attack Flow:
Secure State → Corruption → Redirect → Non-Secure Code Execution (with privileged access)

## Slide 14: ret2ns Attack - Simulation Challenges
gem5 Architectural Limitations:
No standard TrustZone-M extension available
Security-critical branch instructionsincompletely modeled
MPU functionality gaps in simulation framework
System-Level Challenges:
Complex integration of Buildroot with TF-M security framework
Intricate memory domain partitioning requirements
Custom bootloader development necessitated by platform constraints

## Slide 15: Comparison
Spectre Simulation:
Platform | Success | Accuracy | Limitations
gem5 FS Mode | ✓ | High | Timing approximations
gem5 SE Mode | ✗ | N/A | Crashes before completion
QEMU User-Mode | ✓ | High | Limited microarchitecture detail

## Slide 16: Comparison
Ret2ns Simulation:
Aspect | Status | Notes
TrustZone-M Setup | Partial | Requires custom extensions
State Transitions | Limited | Missing BXNS/BLXNS support
MPU Simulation | Incomplete | Manual workarounds needed

## Slide 17: Conclusion
Key Achievements:
✓ Successful Adversary Virtual Platform development for ARM Cortex-M3
✓ Validated Spectre attack in gem5 full-system simulation
✓ Identified critical gaps in TrustZone-M simulation capabilities
✓ Demonstrated cost-effective security evaluation methodology
Future Directions:
Extend gem5 TrustZone-M support
Expand gem5 security extensions

## Slide 18
18/18
Thank you for listening!
Any questions?